## Slide 1
KABETE NATIONAL POLYTECHNIC • COMPUTING AND INFORMATICS
How to configure switches and routers in Packet Tracer
A step-by-step Cisco IOS command-line (CLI) workbook for trainees and trainers
Perform Network Design and Management • Unit code 0612 451 07A • ICT Technician Level 6
Set up
VLANs
DHCP
Routing
Security
Troubleshooting
Trainer: Jacob Kimwele • CBET training slides • October 2026
Notes: Welcome. This workbook pulls the Packet Tracer part of the unit into one place and turns it into step-by-step skills. Every slide starts with “How to…”, so trainees can find a skill fast and practise it alone. Commands are on the left (exactly what to type), the meaning is on the right, and each slide ends with a check and a common mistake.

## Slide 2: How to use this workbook
START HERE
How to configure a router interface
Goal: give R1’s LAN port its gateway address
R1(config)# interface g0/0/0
R1(config-if)# ip address …
R1(config-if)# no shutdown
Select the port
Give it its address
Switch it on
Check it: show ip int brief
Watch out: no shutdown!
1
2
3
4
5
1
Title — the skill
Every slide starts with “How to…”.
2
Goal — what and why
What you will achieve, in one line.
3
Dark column — what to type
Type the white text. The green prompt shows the mode you must be in.
4
Light column — what it means
Each command explained in plain English.
5
Check it / Watch out
Prove it worked, and avoid the usual mistake.
Typing conventions
R1(config)# is the prompt — never type it
Lines that start with ! are notes — skip them
Names, passwords and IPs are lab examples
Short forms work: conf t, int g0/0/0, sh ip int br
Study routine for every slide
Read the goal → build it in Packet Tracer → type the commands → run the check → break it on purpose, then fix it.
Notes: Walk through the anatomy once. Point out that the prompt is not typed, and that every command slide has the same layout, so trainees always know where to look. Encourage the study routine: the “break it and fix it” step builds troubleshooting skill.

## Slide 3: How to find your way: the workbook menu
START HERE
Click a tile to jump to that part. The home button at the bottom right of every slide brings you back here.
01
Packet Tracer basics
02
The IOS command line
03
Basic set-up & SSH
04
VLANs & trunks
05
Inter-VLAN routing
06
DHCP
07
Routing
08
Security & NAT
09
STP & EtherChannel
10
Management & IPv6
11
Troubleshooting
12
Practice & quick reference
Notes: Interactive menu: in Slide Show, click a tile to jump to that part. Every slide has a home button (bottom right) that returns here. Suggested order for a new class: 01 → 12. For revision, jump straight to the part you need.

## Slide 4: How to get started in Packet Tracer
01
Build a network on screen: add devices, choose the right cables, open the command line and test with ping.
In this part, learn how to:
find your way around the workspace
add devices and connect the right cable
open the CLI of a router or switch
give a PC an address and ping
watch packets in Simulation mode
Notes: Part 01 is about the tool, not the commands. Trainees who are confident with Packet Tracer make fewer “mystery” mistakes later (wrong cable, port off, simulation left running).

## Slide 5: How to find your way around the Packet Tracer workspace
01 • PACKET TRACER BASICS
Goal: Know where everything is before you build: six areas you will use in every lab.
Cisco Packet Tracer — Lab2_VLANs_YourName.pkt
File Edit Options View Tools Extensions Window Help
Logical
Physical
R1
S1
PC-A
PC-B
Network Devices › Routers
4331
4321
2911
1941
Realtime
Simulation
▶▶ Fast Forward Time
1
2
3
4
5
6
1
Menu and toolbar
File › Save As, Undo, Zoom.
2
Logical / Physical tabs
Stay in Logical: the network diagram.
3
Workspace
Drag devices here and cable them.
4
Common tools
Select, Inspect, Delete, Note, Draw, Add Simple PDU.
5
Device-Type Selection box
Pick a category, then a model.
6
Realtime / Simulation
Run normally, or step through packets.
Tip: Save often (Ctrl+S): name files like Lab2_VLANs_YourName.pkt
Notes: Open Packet Tracer on the projector and point at each numbered area. Positions move slightly between versions 8.x and 9.x, but the names stay the same — hovering over a button shows its name. Ask trainees to save an empty file with the naming pattern now.

## Slide 6: How to add devices and connect them with the right cable
01 • PACKET TRACER BASICS
Goal: Build the topology on screen. The right cable makes the link light green; the wrong one leaves it red.
1
Add a device
Bottom-left: Network Devices › Routers, then drag a 4331 onto the workspace. Switches › 2960 and End Devices › PC work the same way.
2
Pick a cable
Click Connections (the lightning-bolt icon), then the cable type you need.
3
Connect
Click the first device and choose its port, then click the second device and choose its port.
4
Read the link lights
Green = up. Amber = switch port still starting (wait about 30 s or click Fast Forward Time). Red = down.
Which cable?
Copper Straight-Through — different device types: PC–switch, switch–router
Copper Cross-Over — same device types: switch–switch, router–router, PC–PC (and PC–router)
Console — PC RS 232 port → router or switch Console port, to reach the CLI
Serial DCE / DTE — router–router WAN link (the router needs a serial module)
Fiber — fibre ports: long or fast links between switches
Automatic — Packet Tracer chooses for you — avoid it in assessments
Watch out: Red light on a router link even with the right cable? Router ports stay off until you type no shutdown (part 03).
Notes: Rule of thumb: “different devices – straight; same devices – cross”. A PC and a router count as the same kind (both are hosts), so a direct PC–router link needs a cross-over. Show the amber light on a new switch link and use Fast Forward Time.

## Slide 7: How to open the command line (CLI) of a router or switch
01 • PACKET TRACER BASICS
Goal: Reach the Cisco IOS command line — the way you will configure everything in this workbook.
Quick way — the CLI tab
Click the router or switch → CLI tab → click inside the black window and press Enter.
Real-life way — a console cable
Console cable: PC RS 232 → device Console. Then PC › Desktop › Terminal → OK (keep 9600 bits/s) → press Enter.
The Config tab (a shortcut)
Forms that type commands for you, shown at the bottom as Equivalent IOS Commands. Learn from it, but practise in the CLI.
R1 › CLI (end of the start-up messages)
--- System Configuration Dialog ---
Would you like to enter the initial
configuration dialog? [yes/no]: no
Press RETURN to get started!
Router>enable
Router#
Answer no — you will configure by hand. Router> = user mode (look only); enable takes you to Router#.
Watch out: Nothing on screen? Click inside the CLI window and press Enter — the device may still be starting up.
Notes: Demonstrate both ways. The console method matters because it is how a brand-new real device is configured, and assessors like to see it. Point out the Equivalent IOS Commands box in the Config tab as a learning aid only.

## Slide 8: How to give a PC an IP address and test it with ping
01 • PACKET TRACER BASICS
Goal: Every PC needs an address, mask and default gateway before it can talk. Then prove it with ping.
PC-A › Desktop › IP Configuration
○ DHCP ● Static
IPv4 Address
192.168.1.10
Subnet Mask
255.255.255.0
Default Gateway
192.168.1.1
DNS Server
192.168.50.10
1
Click the PC → Desktop → IP Configuration.
2
Choose Static, type address, mask and gateway (or DHCP — part 06).
3
Close it, open Command Prompt and test.
PC-A › Command Prompt (output shortened)
C:\>ipconfig
IPv4 Address......: 192.168.1.10
Subnet Mask.......: 255.255.255.0
Default Gateway...: 192.168.1.1
C:\>ping 192.168.1.1
Reply from 192.168.1.1: bytes=32 time<1ms TTL=255
Reply from 192.168.1.1: bytes=32 time<1ms TTL=255
...
Packets: Sent = 4, Received = 4, Lost = 0
C:\>tracert 192.168.20.10
! lists every router on the way
Watch out: The first ping may lose one reply while ARP finds the MAC address. That is normal — ping again.
Tip: No typing: Add Simple PDU (closed envelope) → click source → click destination → read the PDU list.
Notes: Make trainees say the three numbers aloud: address, mask, gateway. “Request timed out” means no answer; “Destination host unreachable” means a router said it has no route. Show ipconfig before every ping when troubleshooting.

## Slide 9: How to watch packets travel in Simulation mode
01 • PACKET TRACER BASICS
Goal: Slow the network down and see each packet hop by hop — the best way to understand ARP, DHCP and routing.
1
Click Simulation (bottom-right, next to Realtime).
2
Edit Filters → tick only what you want to see, e.g. ICMP and ARP.
3
Make traffic: Add Simple PDU from PC-A to PC-B, or ping from the Command Prompt.
4
Press Capture/Forward for one step, or Play to run.
5
Click an envelope (or an Event List row) → the OSI Model tab explains each layer.
6
Click Realtime to go back to normal.
PC-A
192.168.1.10
S1
PC-B
192.168.1.11
Time (s) | Last device | At device | Type
0.000 | -- | PC-A | ARP
0.001 | PC-A | S1 | ARP
0.002 | S1 | PC-B | ARP
0.003 | PC-B | S1 | ARP
0.005 | PC-A | S1 | ICMP
Check it: You should see ARP first (“who has 192.168.1.11?”), then the ICMP echo request and reply.
Watch out: Nothing moves? Tick the protocol in Edit Filters, then press Capture/Forward.
Notes: Run one ping in Simulation mode with ARP + ICMP filters. Ask: why does ARP happen first? (The PC knows the IP but not the MAC.) Run it again — no ARP this time, because the ARP table now has the entry. This is also how to see DHCP DORA in part 06.

## Slide 10: How to work in the Cisco IOS command line
02
Every Cisco router and switch speaks IOS. Learn its modes, its built-in help and how to read its messages before you configure anything.
In this part, learn how to:
move between the command modes
get help and type less
read IOS error messages
name interfaces correctly
Notes: Spend time here: most beginner errors are a correct command typed in the wrong mode, or a wrong interface name. The building analogy works well: reception (>), manager’s office (#), workshop (config)#, small rooms (config-if)#.

## Slide 11: How to move between the IOS command modes
02 • THE IOS COMMAND LINE
Goal: IOS is like a building: each room (mode) allows different commands. The prompt tells you which room you are in.
User EXEC
R1>
Look only: basic show, ping
Privileged EXEC
R1#
All show, copy, reload
Global configuration
R1(config)#
Settings for the whole device
enable
configure
terminal
disable
end / exit
interface g0/0/0
R1(config-if)#
One port
line vty 0 4
R1(config-line)#
Console or remote lines
router ospf 10
R1(config-router)#
A routing protocol
vlan 10
S1(config-vlan)#
A VLAN (switch)
ip dhcp pool LAN
R1(dhcp-config)#
A DHCP pool
Typed in global configuration mode, these commands open the smaller “rooms”. exit = one level back; end or Ctrl+Z = straight back to R1#.
Check it: Type ? at any prompt: IOS lists exactly what that mode accepts.
Watch out: Read the prompt before you type. Most errors are the right command in the wrong mode.
Notes: Draw the building on the board. Have trainees move in and out of each mode and say the prompt aloud. Quick drill: “Get me to line configuration for the console” → enable, configure terminal, line console 0. Then “back to privileged mode in one step” → end.

## Slide 12: How to get help and type less in the CLI
02 • THE IOS COMMAND LINE
Goal: IOS has built-in help and shortcuts. Use them and you will type less and make fewer mistakes.
Key or command | What it does | Example
? | List every command or option you can type at this point | R1# show ?
co? | List the commands that start with those letters (no space before ?) | configure connect copy
Tab | Complete a partly typed word | conf + Tab gives configure
Short forms | Any abbreviation that is unique works | conf t, int g0/0/0, sh ip int br
↑ ↓ arrows | Recall the previous or next command | Edit it, then press Enter
end or Ctrl+Z | Jump straight back to privileged mode (#) | R1(config-if)# end → R1#
Ctrl+Shift+6 | Stop a running ping, traceroute or name lookup | When a typo freezes the screen
do | Run a show or copy command without leaving config mode | do show ip int brief
no | Undo (reverse) a command | no shutdown, no ip address
Tip: Learn with ?: type show ? or interface ? and IOS lists exactly what it expects next.
Notes: Make the ? key a habit. A good exercise: give trainees a command they have never seen (e.g. “find the command that shows the clock”) and let them discover it with ? (show clock).

## Slide 13: How to read IOS error messages
02 • THE IOS COMMAND LINE
Goal: Error messages are clues, not failures. Each one tells you what kind of mistake you made.
You typed | IOS replied | Why — and the fix
R1> configure terminal | % Invalid input detected at '^' marker. | You are in user mode (>). Type enable first.
R1(config)# show running-config | % Invalid input detected at '^' marker. | show is not a config command. Use do show running-config.
R1(config-if)# ip address 192.168.1.1 | % Incomplete command. | Something is missing — here the mask. Type ? to see what comes next.
R1# c | % Ambiguous command: "c" | Several commands start with c. Type more letters.
R1# shwo | Translating "shwo"...domain server (255.255.255.255) | IOS thinks the typo is a computer name. Press Ctrl+Shift+6; prevent it with no ip domain-lookup.
R1(config-if)# ip address 192.168.1.5 255.255.255.0 | % 192.168.1.0 overlaps with GigabitEthernet0/0/0 | Two router ports can’t share a subnet. Give this port a different one.
Tip: The ^ marker points at the first character IOS did not understand — look there first.
Notes: Show each error live. Ask trainees to read the message aloud and say what kind of mistake it is (wrong mode, missing value, typo, design error) before fixing it.

## Slide 14: How to name the interfaces you type
02 • THE IOS COMMAND LINE
Goal: Every command that touches a port needs its exact name. The name tells you the type and where the port sits.
GigabitEthernet
type (short: g, fa, s)
/
0
slot
/
0
module bay
/
0
port
Not sure of the name?
Run show ip interface brief — it lists every port your device really has.
Device (Packet Tracer model) | Interface names | Type it as
Router 4331 | GigabitEthernet0/0/0 and 0/0/1. 0/0/2 is an empty slot: power off, add a GLC-T module, power on | g0/0/0
Router 1941 / 2901 / 2911 | GigabitEthernet0/0 and 0/1 (the 2911 also has 0/2) | g0/0
Router + serial module | 4331 + NIM-2T: Serial0/1/0 – 0/1/1. 1941 + HWIC-2T: Serial0/0/0 – 0/0/1 | s0/1/0
Switch 2960-24TT, multilayer 3560-24PS | FastEthernet0/1 – 0/24 and GigabitEthernet0/1 – 0/2 | fa0/1, g0/1
Virtual interfaces | Vlan1, Vlan99 (SVI) • Port-channel1 • g0/0/1.10 (sub-interface) | int vlan 99
Notes: The 4331 catch: in Packet Tracer its third port G0/0/2 is an empty SFP slot. Click the router → Physical tab → power switch off → drag GLC-T into the slot next to G0/0/1 → power on. Labs in this workbook that use G0/0/2 need this step. Modules are always added with the power off.

## Slide 15: How to set up a new router or switch
03
The “starter pack” for every Cisco device: name it, secure it, address it, save it — and manage it safely with SSH. (Lab 1)
In this part, learn how to:
do the basic set-up on any device
save, view and erase a configuration
address a router interface
read show ip interface brief
give a switch a management IP
configure many ports at once
set up SSH remote access
Notes: This part follows Lab 1: R1 (4331), S1 (2960), PC-A and PC-B. Every later lab starts with this starter pack, so drill it until trainees can type it from memory.

## Slide 16: How to do the basic set-up on any router or switch (1 of 2)
03 • BASIC SET-UP & SSH • LAB 1
Goal: Name the device, protect privileged mode and add a legal warning. Do this first on every new device.
● ● ● R1 — type the white text, then press Enter
What it does
Router> enable
Move from user mode (>) to privileged mode (#). Nothing can be configured from >.
Router# configure terminal
Enter global configuration mode. From now on, each command changes the live configuration at once.
Router(config)# hostname R1
Name the device. The prompt becomes R1(config)#, so you always know which device you are on.
R1(config)# no ip domain-lookup
Stop IOS treating a typo as a computer name to look up (it freezes the screen for about 30 seconds).
R1(config)# enable secret Kabete@2026
The password for enable, stored as a secure hash. Never use the old enable password — it is stored as plain text.
R1(config)# banner motd # Authorised access only! #
A legal warning shown to everyone who connects. The # signs mark where the message starts and ends.
Check it: Type end, then disable, then enable again: R1 must now ask for the password.
Watch out: If your message contains #, use another start/end sign, e.g. banner motd $ … $.
Notes: Type along with trainees. Ask before each line: “What will change on the screen?” (for hostname: the prompt). Point out that the same commands work on a switch — only the prompt says Switch instead of Router. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 17: How to do the basic set-up on any router or switch (2 of 2)
03 • BASIC SET-UP & SSH • LAB 1
Goal: Lock the console port, keep messages tidy, hide passwords and save. The same commands work on a switch.
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# line console 0
Open the settings of the console port (the light-blue cable). The prompt becomes (config-line)#.
R1(config-line)# password Cons@1234
Set the console password.
R1(config-line)# login
Make the console ask for that password. Without login, the password is never requested.
R1(config-line)# logging synchronous
Stop system messages from interrupting your typing.
R1(config-line)# exec-timeout 5 0
Log out a session that is idle for 5 minutes 0 seconds.
R1(config-line)# exit
R1(config)# service password-encryption
Back to global mode, then hide the console and VTY passwords in show running-config (weak: it only stops onlookers).
R1(config)# end
R1# copy running-config startup-config
Back to privileged mode, then save your work.
Check it: Type exit to log out, then press Enter: the banner appears and the console asks for a password.
Watch out: Passwords are case-sensitive. Record them in your lab notes — a forgotten secret means password recovery.
Notes: Common mistake: setting the console password but forgetting login. Demonstrate it: remove login, log out, and show that no password is asked. Then put it back. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 18: How to save, view and erase a configuration
03 • BASIC SET-UP & SSH
Goal: The live configuration (RAM) is lost at power-off. The saved one (NVRAM) is loaded at every start-up.
● ● ● R1 — type the white text, then press Enter
What it does
R1# copy running-config startup-config
Save the live configuration to NVRAM so it survives a restart. Press Enter to accept [startup-config].
R1# write memory
A shorter way to make exactly the same save (wr works too).
R1# show running-config
Show the live configuration. Space = next page, Enter = next line, Q = quit.
R1# show startup-config
Show the saved configuration. Anything missing here is not saved yet.
R1# erase startup-config
S1# delete flash:vlan.dat
Wipe the saved configuration to start a lab again. A switch keeps its VLANs in vlan.dat — delete that too.
R1# reload
Restart the device. After an erase, answer no to “Save?” so it starts empty.
Check it: After saving, show startup-config shows your hostname and passwords.
Watch out: Anything not saved is lost when the device reloads or loses power — save after every step that works.
Notes: Saving the .pkt file stores the whole lab, but assessors check that each device’s startup-config is saved too, and real devices need it. Teach both habits: Ctrl+S for the file, copy run start for each device. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 19: How to configure a router interface with an IP address
03 • BASIC SET-UP & SSH • LAB 1
Goal: Give R1’s LAN port an address so the PCs on that LAN can use it as their default gateway (192.168.1.0/24).
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# interface g0/0/0
Select the port (full name GigabitEthernet0/0/0). The prompt becomes (config-if)#.
R1(config-if)# description LAN to S1 - ICT Lab
A label for people. It changes nothing, but helps whoever troubleshoots later.
R1(config-if)# ip address 192.168.1.1 255.255.255.0
The port’s address and subnet mask. PCs on this LAN use 192.168.1.1 as their default gateway.
R1(config-if)# no shutdown
Switch the port on. Router ports start “administratively down” — the number-one cause of red links.
R1(config-if)# exit
Back to global configuration mode.
Check it: show ip interface brief → G0/0/0 192.168.1.1 up up. From PC-A, ping 192.168.1.1 gets replies.
Watch out: Each router port needs its own subnet, and the PCs’ gateway must match this address exactly.
Notes: Ask: why does a router need an IP on each port but a switch does not? (A router joins different networks; a switch forwards inside one.) Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 20: How to read show ip interface brief
03 • BASIC SET-UP & SSH
Goal: The most-used command in this workbook. Each row is a port; two columns tell you what is wrong.
R1 › CLI (shortened)
R1# show ip interface brief
Interface IP-Address OK? Method Status Protocol
GigabitEthernet0/0/0 192.168.1.1 YES manual up up
GigabitEthernet0/0/1 unassigned YES unset administratively down down
Status | Protocol | What it means | Usual fix
up | up | Working: cable and port are fine (Layers 1 and 2) | —
administratively down | down | The port is switched off (never enabled, or shutdown typed) | no shutdown
down | down | No signal: cable missing or wrong type, or the far end is off | Check the cable and the other end
up | down | Signal OK, but the two ends disagree (e.g. encapsulation) | Compare the settings at both ends
Tip: Method: manual = you typed the address, DHCP = it was leased, unset = no address yet.
Notes: Read the output aloud row by row. Then break the network on purpose (unplug a cable, shut a port) and let trainees diagnose from the Status and Protocol columns alone.

## Slide 21: How to give a switch a management IP address
03 • BASIC SET-UP & SSH • LAB 1
Goal: A switch forwards frames without any IP. Give it one only so you can manage it over the network (ping, SSH).
● ● ● S1 — type the white text, then press Enter
What it does
S1(config)# interface vlan 1
Open the switch virtual interface (SVI) of VLAN 1 — a virtual port inside the switch.
S1(config-if)# ip address 192.168.1.2 255.255.255.0
The switch’s management address, in the same subnet as the PCs of that VLAN.
S1(config-if)# no shutdown
SVIs start switched off. It turns up/up once a port in that VLAN is up.
S1(config-if)# exit
Back to global configuration mode.
S1(config)# ip default-gateway 192.168.1.1
Where the switch sends replies for other subnets: R1’s LAN address.
Check it: show ip interface brief → Vlan1 192.168.1.2 up up. PC-A: ping 192.168.1.2 gets replies.
Watch out: A Layer 2 switch has no routing table: without ip default-gateway it can only reply inside its own subnet.
Notes: Contrast with the router: switch ports are on by default and need no IP; only the SVI does. In part 04 the management address moves to VLAN 99. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 22: How to configure many switch ports at once
03 • BASIC SET-UP & SSH • LAB 1
Goal: interface range applies the same commands to a group of ports — faster, and fewer mistakes.
● ● ● S1 — type the white text, then press Enter
What it does
S1(config)# interface range fa0/1 - 24
Select ports Fa0/1 to Fa0/24 together. The prompt becomes (config-if-range)#.
S1(config-if-range)# description USER PORT
Every selected port gets the same label.
S1(config-if-range)# interface range fa0/1 - 5, fa0/10
Mix ranges and single ports, separated by commas.
S1(config-if-range)# interface range fa0/3 - 24, g0/2
S1(config-if-range)# shutdown
Switch off every port you are not using, so nobody can plug in. (Lab 1 uses Fa0/1, Fa0/2 and G0/1.)
S1(config-if-range)# interface fa0/3
S1(config-if)# no shutdown
Re-enable a single port when a new user needs it.
Check it: show ip interface brief lists the unused ports as administratively down.
Watch out: Don’t shut the uplink to the router (G0/1 in Lab 1), or you lose contact with the rest of the network.
Notes: Spaces around the dash are optional in Packet Tracer (fa0/1-24 also works). Shutting unused ports is free, effective security — assessors look for it. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 23: How to set up SSH for secure remote access (1 of 2)
03 • BASIC SET-UP & SSH • LAB 1
Goal: SSH lets you manage a device over the network, encrypted. It needs a hostname, a domain name, a user and RSA keys.
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# ip domain-name knp.ac.ke
Needed to name the encryption keys (R1.knp.ac.ke). RSA keys cannot be made without it.
R1(config)# username netadmin privilege 15 secret N3t@dmin26
A personal admin account stored on the device. Privilege 15 = full control straight after login.
R1(config)# username helpdesk privilege 1 secret H3lp@desk26
A help-desk account: it logs in at R1> (look only) and needs the enable secret to go further.
R1(config)# crypto key generate rsa general-keys modulus 1024
Create the RSA keys that encrypt SSH; this also turns SSH on. Use at least 1024 bits (2048 on real kit).
R1(config)# ip ssh version 2
Allow only SSH version 2 — version 1 has known weaknesses.
Check it: show ip ssh → “SSH Enabled - version 2.0”.
Watch out: “Please define a hostname other than Router” or “…a domain-name first”? Set them, then generate the keys again.
Notes: Remind trainees of the four ingredients: hostname, domain name, user account, RSA keys. If any is missing, SSH will not start. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 24: How to set up SSH for secure remote access (2 of 2)
03 • BASIC SET-UP & SSH • LAB 1
Goal: Tell the remote-access (VTY) lines to accept SSH only, using the local accounts. Then test from a PC.
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# line vty 0 4
Open the 5 virtual lines used by remote sessions (a 2960 switch has 16: line vty 0 15).
R1(config-line)# transport input ssh
Accept SSH only. Telnet is refused because it sends passwords as plain text.
R1(config-line)# login local
Ask for a username and password from the local accounts (the username commands).
R1(config-line)# exec-timeout 5 0
Log out remote sessions that are idle for 5 minutes.
R1(config-line)# end
R1# copy running-config startup-config
Back to privileged mode and save.
C:\> ssh -l netadmin 192.168.1.1
! then type the password (it is not shown)
Test from PC-A › Command Prompt. netadmin lands at R1#; helpdesk lands at R1>.
Check it: From PC-A, SSH works and telnet 192.168.1.1 fails. On a switch, secure line vty 0 15 the same way.
Watch out: Use login local, not login: with login IOS wants a line password you never set, so every login fails.
Notes: Let a trainee log in as helpdesk and try configure terminal — it fails until they enter enable. That shows privilege levels in action. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 25: How to practise: Lab 1 — basic router and switch set-up
03 • BASIC SET-UP & SSH • LAB 1
Goal: Build this network and apply everything in this part. Then prove it works with the checks at the bottom.
R1
4331
S1
2960
PC-A
PC-B
G0/0/0
G0/1
Fa0/1
Fa0/2
console cable
Device | Interface | IP address / mask | Gateway
R1 | G0/0/0 | 192.168.1.1 /24 | —
S1 | VLAN 1 | 192.168.1.2 /24 | 192.168.1.1
PC-A | NIC | 192.168.1.10 /24 | 192.168.1.1
PC-B | NIC | 192.168.1.11 /24 | 192.168.1.1
Tasks
Build and cable it (straight-through; console cable PC-B → R1).
Basic set-up on R1 and S1: hostname, secret, console, banner.
Address R1 G0/0/0, S1 VLAN 1 and both PCs; shut unused ports.
SSH on R1 and S1 (user netadmin); save both devices.
Prove it: all pings work, SSH works, Telnet is refused.
Use the console cable for the first set-up of R1 — the way a brand-new real router is configured.
Notes: Allow about 4 hours including the SSH test. Assess with the checklist: correct cabling, own CLI typing, saved configs, successful tests, and the trainee explaining each command.

## Slide 26: How to separate a network with VLANs
04
Split one switched network into departments — STAFF, STUDENTS, FINANCE — and carry them all between switches over trunks. (Lab 2)
In this part, learn how to:
understand VLANs before you configure
plan the VLAN lab
create and name VLANs
put ports into VLANs
configure trunk links
manage a switch through VLAN 99
check VLANs and trunks
change VLANs safely
Notes: Lab 2 runs through parts 04 and 05: VLANs and trunks first, then router-on-a-stick. Part 06 (Lab 4) adds DHCP to the same file. Save a copy of the .pkt after each part.

## Slide 27: How to understand VLANs before you configure them
04 • VLANS & TRUNKS
Goal: A VLAN turns one physical switch into several separate “rooms”, each with its own subnet.
Without VLANs, a switch is one big room: a broadcast from any PC reaches every PC.
VLANs make separate rooms. A port in VLAN 10 only talks to other VLAN 10 ports.
One VLAN = one subnet. STAFF = 192.168.10.0/24, STUDENTS = 192.168.20.0/24.
Access port — carries one VLAN; for a PC, printer or access point.
Trunk port — carries many VLANs between switches (and to a router); each frame gets an 802.1Q tag with its VLAN number.
Between VLANs you need a router or a Layer 3 switch (part 05).
Think of it like this
One building (switch), separate rooms (VLANs), one shared lift (trunk) that keeps everyone’s badge on (the tag).
TRUNK — carries VLAN 10, 20 and 30 (tagged)
S1
VLAN 10
VLAN 20
VLAN 30
S2
VLAN 10
VLAN 20
VLAN 30
A frame on the trunk:
Dest MAC
Src MAC
802.1Q tag: VLAN 10
Data
The receiving switch reads the tag, removes it and delivers the frame only to VLAN 10 ports.
Notes: Use the building analogy: one floor (switch), walls (VLANs), a lift between floors that carries everyone but keeps their badges (the trunk and its tags). Ask: if VLAN 10 and VLAN 20 PCs are on the same switch, can they ping? (No — not without a router.)

## Slide 28: How to plan the VLAN lab (Lab 2 topology)
04 • VLANS & TRUNKS • LAB 2
Goal: Plan before you type: every VLAN gets a number, a name, a set of ports and its own subnet.
R1
4331
S1
S2
PC1
.10.11
PC2
.20.11
PC3
.30.11
PC4
.10.12
PC5
.20.12
PC6
.30.12
G0/0/1
G0/2
G0/1
G0/1
trunks (native VLAN 99)
PC labels show the end of the address: .10.11 = 192.168.10.11 /24
VLAN | Name | Access ports | Subnet | Gateway
10 | STAFF | Fa0/1 – 10 | 192.168.10.0 /24 | 192.168.10.1
20 | STUDENTS | Fa0/11 – 20 | 192.168.20.0 /24 | 192.168.20.1
30 | FINANCE | Fa0/21 – 24 | 192.168.30.0 /24 | 192.168.30.1
99 | MGMT (native) | none — trunks only | 192.168.99.0 /24 | 192.168.99.1
Good to know
Switch management addresses: S1 = 192.168.99.2, S2 = 192.168.99.3.
Gateways are R1 sub-interfaces (part 05) — the .1 of each VLAN.
The same VLANs must exist on S1 and S2.
Cables: switch–switch cross-over; switch–router straight-through.
Notes: Make trainees copy this plan into their notebooks before building. Assessors expect the plan (VLAN table and addressing) as evidence, and the topology labelled with Notes in Packet Tracer.

## Slide 29: How to create and name VLANs
04 • VLANS & TRUNKS • LAB 2
Goal: Create the four VLANs of the plan on S1 — then do exactly the same on S2.
● ● ● S1 — type the white text, then press Enter
What it does
S1(config)# vlan 10
S1(config-vlan)# name STAFF
Create VLAN 10, enter VLAN mode, and give it a name people understand. Names show in show vlan brief.
S1(config-vlan)# vlan 20
S1(config-vlan)# name STUDENTS
Create the next VLAN straight from VLAN mode — no need to exit first.
S1(config-vlan)# vlan 30
S1(config-vlan)# name FINANCE
VLAN 30 for the finance office.
S1(config-vlan)# vlan 99
S1(config-vlan)# name MGMT
VLAN 99 for managing the switches; it will also be the trunks’ native VLAN.
S1(config-vlan)# end
Back to privileged mode. The VLANs are applied when you leave VLAN mode.
Check it: show vlan brief lists 10 STAFF, 20 STUDENTS, 30 FINANCE and 99 MGMT (no ports yet).
Watch out: VLAN 1 is the default: it cannot be renamed or deleted. Repeat these commands on S2!
Notes: Ask why names matter: six months later nobody remembers that VLAN 30 is finance. Show show vlan brief before and after. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 30: How to put switch ports into a VLAN (access ports)
04 • VLANS & TRUNKS • LAB 2
Goal: Place each user port in its department’s VLAN. A PC plugged into that port joins that VLAN’s subnet.
● ● ● S1 — type the white text, then press Enter
What it does
S1(config)# interface range fa0/1 - 10
Select the ten STAFF ports.
S1(config-if-range)# switchport mode access
Fix them as access ports: one VLAN, for end devices. They can no longer turn themselves into trunks.
S1(config-if-range)# switchport access vlan 10
Put the ports in VLAN 10 (STAFF).
S1(config-if-range)# interface range fa0/11 - 20
S1(config-if-range)# switchport mode access
S1(config-if-range)# switchport access vlan 20
The same three steps for the STUDENTS ports.
S1(config-if-range)# interface range fa0/21 - 24
S1(config-if-range)# switchport mode access
S1(config-if-range)# switchport access vlan 30
And for the FINANCE ports. Then do the same on S2.
Check it: show vlan brief → Fa0/1–10 beside VLAN 10, Fa0/11–20 beside 20, Fa0/21–24 beside 30.
Watch out: A missing VLAN is created for you (“% Access VLAN does not exist. Creating vlan 10”) — but with no name.
Notes: Have trainees give PC1 and PC4 (both VLAN 10) addresses and ping: it works across the switches only after the trunk on the next slide is up. PC1 to PC2 (different VLANs) must fail until part 05. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 31: How to configure a trunk link
04 • VLANS & TRUNKS • LAB 2
Goal: Links between switches, and to the router, must carry every VLAN. Make them 802.1Q trunks — at both ends.
● ● ● S1 — type the white text, then press Enter
What it does
S1(config)# interface range g0/1 - 2
Select both uplinks: G0/1 goes to S2, G0/2 goes to R1.
S1(config-if-range)# switchport mode trunk
Make them trunks: they carry all VLANs, tagging each frame with its VLAN number (802.1Q).
S1(config-if-range)# switchport trunk native vlan 99
Untagged frames now belong to VLAN 99 instead of VLAN 1 — safer. Both ends of a link must agree.
S1(config-if-range)# switchport trunk allowed vlan 10,20,30,99
Only these VLANs may cross the trunk.
S2(config)# interface g0/1
S2(config-if)# switchport mode trunk
S2(config-if)# switchport trunk native vlan 99
S2(config-if)# switchport trunk allowed vlan 10,20,30,99
The same on S2’s uplink to S1 — a trunk has two ends!
Check it: show interfaces trunk → G0/1 and G0/2: mode on, status trunking, native vlan 99.
Watch out: On a 3560, type switchport trunk encapsulation dot1q before switchport mode trunk.
Notes: Now PC1 can ping PC4 (same VLAN, different switches). Break it on purpose: remove VLAN 10 from the allowed list on one end and watch the ping fail. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 32: How to manage a switch through VLAN 99
04 • VLANS & TRUNKS • LAB 2
Goal: Move each switch’s management address out of VLAN 1 into the MGMT VLAN, away from user traffic.
● ● ● S1 — type the white text, then press Enter
What it does
S1(config)# interface vlan 99
Open the SVI of the management VLAN.
S1(config-if)# ip address 192.168.99.2 255.255.255.0
S1’s management address (S2 uses 192.168.99.3).
S1(config-if)# no shutdown
Switch the SVI on.
S1(config-if)# exit
S1(config)# ip default-gateway 192.168.99.1
R1’s VLAN 99 sub-interface (part 05) is the way out for management traffic.
S1(config)# interface vlan 1
S1(config-if)# shutdown
Optional: switch off the unused VLAN 1 interface so it is not used by mistake.
Check it: show ip interface brief → Vlan99 192.168.99.2 up up (once a trunk carrying VLAN 99 is up).
Watch out: Vlan99 stays down until VLAN 99 exists on the switch and a port or trunk carrying it is up.
Notes: After part 05 is finished, SSH from PC1 to 192.168.99.2 to prove the management VLAN works through the router. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 33: How to check VLANs and trunks
04 • VLANS & TRUNKS • LAB 2
Goal: Two show commands prove the VLAN design is built correctly. Learn to read them line by line.
S1 › CLI (columns shortened)
S1# show vlan brief
VLAN Name Status Ports
---- -------------- --------- -------------------------
1 default active
10 STAFF active Fa0/1, Fa0/2, Fa0/3 ...
20 STUDENTS active Fa0/11, Fa0/12 ...
30 FINANCE active Fa0/21, Fa0/22, Fa0/23, Fa0/24
99 MGMT active
S1# show interfaces trunk
Port Mode Encapsulation Status Native vlan
Gig0/1 on 802.1q trunking 99
Gig0/2 on 802.1q trunking 99
Port Vlans allowed on trunk
Gig0/1 10,20,30,99
Gig0/2 10,20,30,99
Ports beside the right VLAN
The access ports are correct. Trunk ports never appear in this list — that is normal.
trunking + native vlan 99
The trunk is up and both ends agree on the native VLAN.
Vlans allowed on trunk
Only these VLANs can cross. A missing VLAN here means its PCs can’t reach the other switch.
Same-VLAN ping fails? Check the VLAN exists on both switches.
Notes: Trainees often panic that trunk ports are missing from show vlan brief. Explain that trunks belong to all allowed VLANs, so they are listed in show interfaces trunk instead.

## Slide 34: How to change, add or remove VLANs safely
04 • VLANS & TRUNKS • LAB 2
Goal: Networks change. Edit VLAN membership and trunk lists without cutting off users who are already working.
● ● ● S1 — type the white text, then press Enter
What it does
S1(config-if)# switchport trunk allowed vlan add 40
Add VLAN 40 to a trunk’s list. Without the word add, the list is replaced and the other VLANs stop crossing!
S1(config-if)# switchport trunk allowed vlan remove 30
Take just VLAN 30 off the trunk.
S1(config)# interface fa0/5
S1(config-if)# switchport access vlan 20
Move one port to another VLAN: re-type the command with the new number.
S1(config-if)# no switchport access vlan
Send the port back to VLAN 1 (the default).
S1(config)# no vlan 30
Delete VLAN 30. Its ports become inactive — move them to another VLAN first.
Check it: Run show vlan brief and show interfaces trunk after every change.
Watch out: Ports left in a deleted VLAN go silent: their PCs lose the network with no error message.
Notes: Troubleshooting-log example (Lab 8): “PC3 cannot ping PC6 → show interfaces trunk → VLAN 30 not allowed → switchport trunk allowed vlan add 30 → PASS”. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 35: How to let VLANs talk to each other
05
VLANs are separate subnets, so traffic between them must be routed. Use router-on-a-stick (Lab 2) or a Layer 3 switch.
In this part, learn how to:
choose an inter-VLAN routing method
configure router-on-a-stick
follow a packet between VLANs
route on a Layer 3 switch
Notes: Continue the Lab 2 file. Before starting, prove the problem: PC1 (VLAN 10) cannot ping PC2 (VLAN 20). After this part, it can.

## Slide 36: How to choose an inter-VLAN routing method
05 • INTER-VLAN ROUTING
Goal: Three ways to route between VLANs. Labs use the first two; know all three for the assessment.
1 trunk
Router-on-a-stick
One router port + one trunk; a sub-interface per VLAN (g0/0/1.10).
✔ Cheap — one cable
✘ All inter-VLAN traffic shares one link
Use: small sites and labs (Lab 2)
Layer 3 switch (SVIs)
The switch routes inside itself; interface vlan 10 is VLAN 10’s gateway.
✔ Fast and scalable
✘ Needs a multilayer switch (3560)
Use: campus core / distribution
1 cable per VLAN
One router port per VLAN
Each VLAN gets its own physical router port and its own cable.
✔ Simple to understand
✘ Runs out of router ports quickly
Use: rarely — old designs
Tip: Whatever the method, each PC’s default gateway is the router or SVI address in its own VLAN (the .1).
Notes: Ask which method a school with 40 VLANs should use (Layer 3 switch) and which a small office with one router should use (router-on-a-stick). The legacy method is examined as a comparison point.

## Slide 37: How to configure router-on-a-stick (1 of 2)
05 • INTER-VLAN ROUTING • LAB 2
Goal: R1 routes between the VLANs over one trunk to S1. Each VLAN gets a sub-interface on G0/0/1.
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# interface g0/0/1
R1(config-if)# no shutdown
Switch on the physical port that connects to S1’s trunk. It gets no IP address itself.
R1(config-if)# interface g0/0/1.10
Create sub-interface 10, a virtual port inside G0/0/1. Matching the number to the VLAN avoids confusion.
R1(config-subif)# description STAFF gateway
A label for people.
R1(config-subif)# encapsulation dot1Q 10
The key command: this sub-interface handles frames tagged VLAN 10. Type it before the IP address.
R1(config-subif)# ip address 192.168.10.1 255.255.255.0
The default gateway of every STAFF PC.
Check it: show ip interface brief → G0/0/1 and G0/0/1.10 are both up up.
Watch out: IOS refuses the IP address until encapsulation dot1Q is set — always type it first.
Notes: Draw the “stick”: one cable, many VLANs. Each sub-interface is a door for one VLAN. The number after the dot is only a label; the dot1Q number is what really matters. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 38: How to configure router-on-a-stick (2 of 2)
05 • INTER-VLAN ROUTING • LAB 2
Goal: Add a sub-interface for every other VLAN — including the native management VLAN — then test across VLANs.
● ● ● R1 — type the white text, then press Enter
What it does
R1(config-subif)# interface g0/0/1.20
R1(config-subif)# encapsulation dot1Q 20
R1(config-subif)# ip address 192.168.20.1 255.255.255.0
The gateway of the STUDENTS VLAN.
R1(config-subif)# interface g0/0/1.30
R1(config-subif)# encapsulation dot1Q 30
R1(config-subif)# ip address 192.168.30.1 255.255.255.0
The gateway of the FINANCE VLAN.
R1(config-subif)# interface g0/0/1.99
R1(config-subif)# encapsulation dot1Q 99 native
R1(config-subif)# ip address 192.168.99.1 255.255.255.0
The MGMT gateway. native = untagged frames belong here; it must match the trunk’s native VLAN on S1.
R1(config-subif)# end
R1# copy running-config startup-config
Finish and save.
Check it: show ip route connected → four C routes (VLANs 10, 20, 30, 99). PC1 (VLAN 10) pings PC2 (VLAN 20).
Watch out: S1’s port to R1 (G0/2) must be a trunk, and each PC’s gateway must be the .1 of its own VLAN.
Notes: Test matrix: PC1→PC2, PC1→PC3, PC2→PC6, and from PC1 ping 192.168.99.2 (S1 management). Then SSH from PC1 to S1 through the router. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 39: How to follow a packet from VLAN 10 to VLAN 20
05 • INTER-VLAN ROUTING • LAB 2
Goal: Understand what router-on-a-stick really does: the packet goes up the trunk and comes back down it.
R1
G0/0/1.10 and .20
S1
PC1 — VLAN 10
192.168.10.11
PC2 — VLAN 20
192.168.20.11
tag 10
tag 20
1
2
3
4
5
1
PC1 sends to 192.168.20.11 — another subnet — so it sends to its gateway, 192.168.10.1.
2
S1 receives it on Fa0/1 (VLAN 10) and sends it up the trunk tagged 10.
3
R1’s sub-interface G0/0/1.10 accepts tag 10, looks up 192.168.20.0 and finds it on G0/0/1.20.
4
R1 sends the packet back down the same cable, tagged 20.
5
S1 removes the tag and delivers it out Fa0/11 (VLAN 20) to PC2.
Tip: See it yourself: Simulation mode, filter ICMP, ping PC1 → PC2, and open the envelope on the trunk to see the 802.1Q tag.
Notes: Run this in Simulation mode. Click the PDU on the trunk link going up and coming down: the 802.1Q VLAN number changes from 10 to 20. That is the whole idea of router-on-a-stick.

## Slide 40: How to route between VLANs on a Layer 3 switch
05 • INTER-VLAN ROUTING
Goal: A multilayer switch (3560) can be the gateway for every VLAN itself — faster than router-on-a-stick.
● ● ● MLS1 — type the white text, then press Enter
What it does
MLS1(config)# ip routing
Turn on routing inside the switch. Without it the SVIs cannot route between VLANs.
MLS1(config)# vlan 10
MLS1(config-vlan)# name STAFF
MLS1(config-vlan)# vlan 20
MLS1(config-vlan)# name STUDENTS
MLS1(config-vlan)# exit
Create the VLANs on the multilayer switch too.
MLS1(config)# interface vlan 10
MLS1(config-if)# ip address 192.168.10.1 255.255.255.0
MLS1(config-if)# no shutdown
The SVI of VLAN 10 is now the default gateway of the STAFF PCs.
MLS1(config-if)# interface vlan 20
MLS1(config-if)# ip address 192.168.20.1 255.255.255.0
MLS1(config-if)# no shutdown
The same for VLAN 20 (STUDENTS). Access ports are set exactly as in part 04.
Check it: show ip route lists both VLAN subnets as C (connected via Vlan10 and Vlan20); the PCs ping each other.
Watch out: On a 3560, no switchport turns a port into a routed port, and trunks need switchport trunk encapsulation dot1q first.
Notes: Build a small separate file for this: one 3560, two PCs in VLAN 10 and 20 on its access ports. In the capstone project the core switch works this way, with ip helper-address on each SVI for DHCP. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 41: How to hand out IP addresses automatically with DHCP
06
Let the router lease addresses, masks, gateways and DNS servers to every PC — for one LAN, for every VLAN, and across subnets with a relay. (Lab 4, built on the Lab 2 file)
In this part, learn how to:
understand the DORA conversation
make a router a DHCP server
give every VLAN its own pool
check the leases
relay DHCP to a server
fix common DHCP problems
Notes: Lab 4 here builds on the Lab 2 file: add a server LAN on R1 G0/0/0 (192.168.50.0/24: SRV1 = 192.168.50.10 for DNS/web, SRV2 = 192.168.50.11 for DHCP) and a LIBRARY LAN on R1 G0/0/2 (192.168.40.0/24). On a 4331, G0/0/2 needs a GLC-T module first.

## Slide 42: How to understand DHCP: the DORA conversation
06 • DHCP
Goal: A PC with no address asks for one. Four messages later it has an address, mask, gateway and DNS server.
PC (client)
no address yet
R1
DHCP server
1 Discover (broadcast): “Is there a DHCP server?”
2 Offer: “You can have 192.168.10.21”
3 Request (broadcast): “I’ll take 192.168.10.21”
4 Acknowledge: “It’s yours — mask, gateway, DNS, lease”
What the PC receives
IP address, subnet mask, default gateway and DNS server (plus domain name and lease time).
DHCP or static?
DHCP: PCs, laptops, phones. Static: routers, switches, servers, printers — keep their addresses out of the pool.
A good plan for each /24 subnet
.1 = gateway • .2 – .20 = static devices • .21 – .254 = DHCP pool
Watch out: A PC showing 169.254.x.x got no DHCP answer — it gave itself an automatic (APIPA) address.
Notes: Watch DORA in Simulation mode: filter DHCP only, set a PC to DHCP, and step through the four messages. Ask why Discover and Request are broadcasts (the PC has no address and does not know the server yet).

## Slide 43: How to configure a router as a DHCP server (1 of 2)
06 • DHCP • LAB 4
Goal: R1 will lease addresses to the STAFF PCs in VLAN 10 (192.168.10.0/24), keeping .1–.20 for static devices.
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# ip dhcp excluded-address 192.168.10.1 192.168.10.20
Never lease .1 to .20 — they are kept for the gateway, servers, printers and switches. Do this before the pool.
R1(config)# ip dhcp pool STAFF-POOL
Create a pool (you choose the name) and enter (dhcp-config)# mode.
R1(dhcp-config)# network 192.168.10.0 255.255.255.0
The subnet to lease from: .21 to .254 after the exclusions.
R1(dhcp-config)# default-router 192.168.10.1
The default gateway given to clients: the router’s own address on that LAN.
R1(dhcp-config)# dns-server 192.168.50.10
The DNS server clients use to turn names into IP addresses.
Check it: show ip dhcp pool → STAFF-POOL, with the number of leased addresses.
Watch out: A wrong default-router lets PCs get an address but never leave their own subnet.
Notes: Stress the order: exclusions first, then the pool. If the pool exists first, a PC may lease an address that you meant to give a printer. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 44: How to configure a router as a DHCP server (2 of 2)
06 • DHCP • LAB 4
Goal: Finish the pool, then switch the PCs to DHCP and check that they lease their addresses.
● ● ● R1 — type the white text, then press Enter
What it does
R1(dhcp-config)# domain-name knp.local
The DNS suffix added to short names (www becomes www.knp.local).
R1(dhcp-config)# exit
Back to global configuration mode.
! On each PC: Desktop › IP Configuration › DHCP
The PC asks for an address. “DHCP request successful” appears and the fields fill in by themselves.
C:\> ipconfig /all
Shows the leased address, mask, gateway, DNS server and the PC’s MAC (Physical Address).
R1# show ip dhcp binding
One line per lease: the IP given out and the MAC of the PC that has it.
Check it: Each STAFF PC gets 192.168.10.21 or higher, gateway 192.168.10.1 and DNS 192.168.50.10.
Watch out: Select DHCP in IP Configuration first; ipconfig /release and /renew then get a fresh lease.
Notes: If a PC keeps “Requesting IP address”, check the VLAN of its switch port and the trunk to R1 — the DHCP request has to reach the right sub-interface. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 45: How to give every VLAN its own DHCP pool
06 • DHCP • LAB 4
Goal: One router can serve every VLAN. It picks the pool whose network matches the sub-interface the request came in on.
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# ip dhcp excluded-address 192.168.20.1 192.168.20.20
R1(config)# ip dhcp excluded-address 192.168.30.1 192.168.30.20
Keep the first 20 addresses of each VLAN for static devices.
R1(config)# ip dhcp pool STUDENT-POOL
R1(dhcp-config)# network 192.168.20.0 255.255.255.0
R1(dhcp-config)# default-router 192.168.20.1
R1(dhcp-config)# dns-server 192.168.50.10
The pool for VLAN 20. Its gateway is sub-interface G0/0/1.20.
R1(dhcp-config)# ip dhcp pool FINANCE-POOL
R1(dhcp-config)# network 192.168.30.0 255.255.255.0
R1(dhcp-config)# default-router 192.168.30.1
R1(dhcp-config)# dns-server 192.168.50.10
The pool for VLAN 30. Its gateway is G0/0/1.30.
Check it: PCs in VLANs 10, 20 and 30 each lease an address from their own subnet; show ip dhcp binding lists them all.
Watch out: No pool for VLAN 99: switches and routers keep static addresses.
Notes: Ask: how does R1 know which pool to use? The request arrives on G0/0/1.20, whose address is 192.168.20.1, so R1 uses the pool whose network contains that address. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 46: How to check DHCP leases on the router and the PC
06 • DHCP • LAB 4
Goal: Match what the router handed out with what the PC received. The MAC address links the two.
R1 › CLI (columns shortened)
R1# show ip dhcp binding
IP address Hardware address Type
192.168.10.21 0060.4721.6A1B Automatic
192.168.20.21 00D0.97C4.3A02 Automatic
192.168.30.21 0001.C7A3.11F5 Automatic
R1# show ip dhcp pool
Pool STAFF-POOL :
Total addresses : 254
Leased addresses : 1
Excluded addresses : 20
PC1 › Command Prompt (shortened)
C:\>ipconfig /all
FastEthernet0 Connection:(default port)
Physical Address....: 0060.4721.6A1B
IPv4 Address........: 192.168.10.21
Subnet Mask.........: 255.255.255.0
Default Gateway.....: 192.168.10.1
DHCP Servers........: 192.168.10.1
DNS Servers.........: 192.168.50.10
Match the MAC
The Hardware address in the binding is the PC’s Physical Address: now you know who has which IP.
Leased addresses
Counts up as PCs join. Still 0 while PCs wait? Their requests are not reaching R1.
Renew a lease
On the PC: ipconfig /release, then ipconfig /renew (DHCP must be selected).
Notes: Have trainees find their own PC in the binding table by matching MAC addresses. This is also the quickest way to find a device that has “disappeared” on a real network.

## Slide 47: How to relay DHCP from another subnet (ip helper-address)
06 • DHCP • LAB 4
Goal: The LIBRARY LAN (192.168.40.0/24) gets its addresses from SRV2, a DHCP server in another subnet.
LIB-PC
R1
SRV2
192.168.50.11
DHCP Discover — a broadcast
forwarded as a unicast to 192.168.50.11
LIBRARY LAN 192.168.40.0/24
G0/0/2 .40.1
G0/0/0 .50.1
SERVER LAN 192.168.50.0/24
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# interface g0/0/2
R1(config-if)# ip address 192.168.40.1 255.255.255.0
R1(config-if)# no shutdown
The LIBRARY port — the clients’ gateway. (On a 4331, add a GLC-T module to G0/0/2 first.)
R1(config-if)# ip helper-address 192.168.50.11
Routers drop broadcasts. This catches the DHCP broadcast and forwards it to SRV2, stamped with 192.168.40.1 so SRV2 picks the right pool.
On SRV2: Services › DHCP
Service On • Pool Name LIB-POOL • Default Gateway 192.168.40.1 • DNS Server 192.168.50.10 • Start IP 192.168.40.100 • Mask 255.255.255.0 • Maximum Users 50 → Add
Watch out
Helper goes on the port facing the clients. SRV2 needs gateway 192.168.50.1 to reply.
Notes: This is how large networks work: one central DHCP server, and a helper address on every client-facing router interface or SVI. Show the relayed Discover in Simulation mode: it leaves R1 as a unicast from 192.168.40.1. Click-to-reveal: each click shows the next explanation. Before each click, ask a trainee to predict what the command does.

## Slide 48: How to fix common DHCP problems
06 • DHCP
Goal: Most DHCP faults are not in the pool at all — they are VLAN, trunk, gateway or relay mistakes.
What you see | Most likely cause | How to fix it
PC address is 169.254.x.x | No DHCP reply reached the PC | Check the pool network, the port’s VLAN, the trunk’s allowed VLANs, and the helper address
PC has an address but cannot leave its subnet | Wrong default-router in the pool | Set it to the router’s address in that subnet, then renew the lease
PC gets an address from the wrong subnet | Its switch port is in the wrong VLAN | switchport access vlan with the right VLAN number
Two devices with the same address | A static device’s address is not excluded | Add ip dhcp excluded-address for it, then renew the PCs
Websites work by IP but not by name | Missing or wrong dns-server | Fix dns-server in the pool and renew the lease
Relay clients get nothing | Helper on the wrong port, or the server has no route back | Helper on the client-side port; give the server a default gateway
Tip: Prove every fix: ipconfig /renew on the PC, then show ip dhcp binding on the router.
Notes: Fault-finding game: inject one of these faults into a trainee’s file and let a partner diagnose it using only the What you see column, show commands and ipconfig.

## Slide 49: How to connect networks with routing
07
Teach routers where every network is — by hand with static routes, or automatically with OSPF, RIP and EIGRP. (Lab 3)
In this part, learn how to:
set up the routing lab
read a routing table
configure static and default routes
configure single-area OSPF
configure RIPv2 and EIGRP
check and troubleshoot routing
Notes: Lab 3: three 4331 routers in a triangle joined by /30 links, each with its own LAN. Do the parts in order and remove each method before the next, because the route with the lowest administrative distance always wins.

## Slide 50: How to set up the routing lab (Lab 3 topology)
07 • ROUTING • LAB 3
Goal: Three routers, three LANs, three point-to-point links. Every link is its own /30 subnet.
R1
R2
R3
PC1
172.16.1.10
PC2
172.16.2.10
PC3
172.16.3.10
10.0.0.0/30
10.0.0.4/30
10.0.0.8/30
LAN 1 172.16.1.0/24
LAN 2 172.16.2.0/24
LAN 3 172.16.3.0/24
Router | G0/0/0 (LAN) | G0/0/1 | G0/0/2
R1 | 172.16.1.1 /24 | 10.0.0.1 /30 → R2 | 10.0.0.9 /30 → R3
R2 | 172.16.2.1 /24 | 10.0.0.2 /30 → R1 | 10.0.0.5 /30 → R3
R3 | 172.16.3.1 /24 | 10.0.0.6 /30 → R2 | 10.0.0.10 /30 → R1
Order of work
Router–router links: cross-over cables. Add a GLC-T module to each G0/0/2.
Address every interface and no shutdown; PCs use their router’s .1 as gateway.
Ping each neighbour across every /30 link before any routing.
Then: static → OSPF → RIP → EIGRP. Remove each before the next, e.g. no router ospf 10.
Notes: A /30 has exactly two usable addresses — one for each router on the link. Ask trainees to work out the four addresses of 10.0.0.4/30 (network .4, R2 .5, R3 .6, broadcast .7).

## Slide 51: How to read a routing table
07 • ROUTING • LAB 3
Goal: show ip route is the router’s map. Each line tells you how a network was learned and which way to send packets.
R1 › CLI (shortened — OSPF running)
R1# show ip route
Codes: L - local, C - connected, S - static, R - RIP,
O - OSPF, D - EIGRP, * - candidate default
Gateway of last resort is not set
C 10.0.0.0/30 is directly connected, GigabitEthernet0/0/1
L 10.0.0.1/32 is directly connected, GigabitEthernet0/0/1
C 172.16.1.0/24 is directly connected, GigabitEthernet0/0/0
L 172.16.1.1/32 is directly connected, GigabitEthernet0/0/0
O 172.16.2.0/24 [110/2] via 10.0.0.2, 00:01:12, GigabitEthernet0/0/1
O 172.16.3.0/24 [110/2] via 10.0.0.10, 00:01:12, GigabitEthernet0/0/2
Code letter
How the route was learned: C connected, L the router’s own address, S static, O OSPF, R RIP, D EIGRP, S* default.
[110/2]
[administrative distance / metric]. Lower distance = more trusted source; lower metric = better path.
via 10.0.0.2 • G0/0/1
The next-hop router, and the port the packet leaves by.
Gateway of last resort
The default route. “not set” = packets to unknown networks are dropped.
Administrative distance — the lower number wins:
0 Connected
1 Static
90 EIGRP
110 OSPF
120 RIP
If two methods know the same network, only the lowest distance goes into the table — that is why each lab part removes the previous method.
Notes: Analogy: the routing table is the signboards at a junction — “Nakuru: left, Mombasa: right”. The default route is the board that says “everywhere else: take the highway”.

## Slide 52: How to configure static routes
07 • ROUTING • LAB 3
Goal: Tell each router by hand where the networks it is not connected to are (Lab 3, part A).
● ● ● R1 / R2 / R3 — type the white text, then press Enter
What it does
R1(config)# ip route 172.16.2.0 255.255.255.0 10.0.0.2
To reach LAN 2, send packets to R2 (10.0.0.2, its address on our shared link). Parts: network, mask, next hop.
R1(config)# ip route 172.16.3.0 255.255.255.0 10.0.0.10
To reach LAN 3, send packets to R3.
R1(config)# ip route 172.16.2.0 255.255.255.0 10.0.0.10 5
A floating static route: a backup path to LAN 2 via R3 with distance 5, used only if the main route (distance 1) fails.
R2(config)# ip route 172.16.1.0 255.255.255.0 10.0.0.1
R2(config)# ip route 172.16.3.0 255.255.255.0 10.0.0.6
R2(config)# ip route 172.16.1.0 255.255.255.0 10.0.0.6 5
R2 needs routes too — every router needs a route there and back — plus its own floating backup to LAN 1 via R3.
R3(config)# ip route 172.16.1.0 255.255.255.0 10.0.0.9
R3(config)# ip route 172.16.2.0 255.255.255.0 10.0.0.5
R3’s routes to LAN 1 and LAN 2.
Check it: show ip route static shows S routes; PC1 pings PC2 and PC3. Shut R1 G0/0/1: the floating routes take over.
Watch out: The next hop is the neighbour’s address on the shared link — never your own address or the neighbour’s LAN address.
Notes: Test the floating route: shut R1’s G0/0/1 and look at show ip route — the S route via 10.0.0.10 appears. No shut it again and the original route returns. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 53: How to configure a default route
07 • ROUTING
Goal: A default route catches every destination the router doesn’t know — usually “all Internet traffic: go to the ISP”.
● ● ● R1 / R2 — type the white text, then press Enter
What it does
R1(config)# ip route 0.0.0.0 0.0.0.0 203.0.113.1
“Anything I don’t know, send to the ISP router 203.0.113.1.” 0.0.0.0 0.0.0.0 matches every address.
R2(config)# ip route 0.0.0.0 0.0.0.0 10.0.0.1
A branch router with only one way out needs just this one route instead of many static routes.
R1(config)# router ospf 10
R1(config-router)# default-information originate
With OSPF running, R1 shares its default route, so the other routers learn it automatically (as O*E2).
R1# show ip route
Look for S* 0.0.0.0/0 [1/0] via 203.0.113.1 and “Gateway of last resort is 203.0.113.1”.
Check it: From a PC, tracert to an Internet server: the trace passes R1 and then the ISP router.
Watch out: Point the default route only at the real exit. Two routers defaulting to each other bounce packets until they expire.
Notes: The ISP link appears in Lab 6 (part 08) and in Challenge lab B. In Lab 3, try the branch idea: replace R2’s static routes with one default route to R1. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 54: How to configure OSPF (single area) (1 of 2)
07 • ROUTING • LAB 3
Goal: OSPF lets routers find every network by themselves and reroute when a link fails (Lab 3, part B — R1 shown).
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# router ospf 10
Start OSPF process 10. The number is local — neighbours don’t need to match it.
R1(config-router)# router-id 1.1.1.1
A unique ID for R1 (R2 = 2.2.2.2, R3 = 3.3.3.3) that makes outputs easy to read.
R1(config-router)# network 172.16.1.0 0.0.0.255 area 0
Run OSPF on the port in 172.16.1.0/24 and put it in area 0. 0.0.0.255 is the wildcard of 255.255.255.0.
R1(config-router)# network 10.0.0.0 0.0.0.3 area 0
R1(config-router)# network 10.0.0.8 0.0.0.3 area 0
Run OSPF on both /30 links (wildcard 0.0.0.3).
R1(config-router)# passive-interface g0/0/0
No OSPF hellos to the PCs, but the LAN is still advertised.
Check it: show ip ospf neighbor → 2.2.2.2 and 3.3.3.3 in FULL state; show ip route ospf → O routes.
Watch out: Remove the static routes first (no ip route …) — with distance 1 they would hide the OSPF routes.
Notes: Wildcard trick: 255.255.255.255 minus the subnet mask. For /24: 0.0.0.255; for /30: 0.0.0.3. The next slide has R2 and R3 in full. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 55: How to configure OSPF (single area) (2 of 2)
07 • ROUTING • LAB 3
Goal: The same pattern on R2 and R3: their own router ID, their own LAN and their two links.
R2 › CLI
R2(config)# router ospf 10
R2(config-router)# router-id 2.2.2.2
R2(config-router)# network 172.16.2.0 0.0.0.255 area 0
R2(config-router)# network 10.0.0.0 0.0.0.3 area 0
R2(config-router)# network 10.0.0.4 0.0.0.3 area 0
R2(config-router)# passive-interface g0/0/0
R3 › CLI
R3(config)# router ospf 10
R3(config-router)# router-id 3.3.3.3
R3(config-router)# network 172.16.3.0 0.0.0.255 area 0
R3(config-router)# network 10.0.0.4 0.0.0.3 area 0
R3(config-router)# network 10.0.0.8 0.0.0.3 area 0
R3(config-router)# passive-interface g0/0/0
Work out the wildcard: 255.255.255.255 − subnet mask
Prefix | Subnet mask | Wildcard
/24 | 255.255.255.0 | 0.0.0.255
/26 | 255.255.255.192 | 0.0.0.63
/30 | 255.255.255.252 | 0.0.0.3
Check it on every router
show ip protocols lists the networks OSPF is running on
show ip ospf neighbor shows two neighbours in FULL state
Each PC can ping the other two PCs
Notes: Common errors: typing the subnet mask instead of the wildcard (OSPF accepts it but matches nothing useful), or a network statement that does not cover the link. show ip protocols reveals both.

## Slide 56: How to check OSPF neighbours and routes
07 • ROUTING • LAB 3
Goal: Two commands prove OSPF works: the neighbours are FULL and the remote LANs appear as O routes.
R1 › CLI
R1# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
2.2.2.2 1 FULL/DR 00:00:35 10.0.0.2 GigabitEthernet0/0/1
3.3.3.3 1 FULL/BDR 00:00:33 10.0.0.10 GigabitEthernet0/0/2
R1# show ip route ospf
O 172.16.2.0/24 [110/2] via 10.0.0.2, 00:02:10, GigabitEthernet0/0/1
O 172.16.3.0/24 [110/2] via 10.0.0.10, 00:02:10, GigabitEthernet0/0/2
O 10.0.0.4/30 [110/2] via 10.0.0.2, 00:02:10, GigabitEthernet0/0/1
[110/2] via 10.0.0.10, 00:02:10, GigabitEthernet0/0/2
FULL
The routers have swapped their complete maps. INIT, 2WAY or no line at all? Check areas, wildcards and passive ports. DR/BDR is just the neighbour’s role on that link.
[110/2]
OSPF’s distance (110) and cost (2): 1 for the link to R2 plus 1 for R2’s LAN — each Gigabit link costs 1.
Two “via” lines
Two paths with the same cost: OSPF shares traffic across both (equal-cost load balancing).
Notes: Failover test: start ping -t from PC1 to PC2, then shut R1 G0/0/1. OSPF reroutes through R3 after a few lost replies. Compare with the static lab, where nothing happens without the floating route.

## Slide 57: How to configure RIP version 2
07 • ROUTING • LAB 3
Goal: RIP is the simplest routing protocol — fine for small networks. First remove OSPF: no router ospf 10 (part C).
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# router rip
Start RIP and enter (config-router)# mode.
R1(config-router)# version 2
Use RIPv2: it sends subnet masks (needed for /30 and /24 subnets) and uses multicast.
R1(config-router)# no auto-summary
Advertise the real subnets, not the summary 172.16.0.0/16.
R1(config-router)# network 172.16.0.0
Run RIP on the ports in 172.16.x.x. RIP takes classful network numbers — no mask.
R1(config-router)# network 10.0.0.0
Run RIP on both 10.0.0.x links.
R1(config-router)# passive-interface g0/0/0
No RIP updates to the PCs; the LAN is still advertised.
Check it: show ip route rip → R 172.16.2.0/24 [120/1] via 10.0.0.2 (120 = RIP’s distance, 1 = one hop).
Watch out: network means “run RIP on my ports in this network”, not “route to it”. RIP gives up after 15 hops.
Notes: Same commands on R2 and R3 — with RIP the network statements are identical on all three routers (172.16.0.0 and 10.0.0.0). RIP updates every 30 seconds; use Fast Forward Time. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 58: How to configure EIGRP
07 • ROUTING • LAB 3
Goal: EIGRP is Cisco’s fast-converging protocol. First remove RIP: no router rip (part D).
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# router eigrp 100
Start EIGRP in autonomous system 100. Every neighbour must use the same number.
R1(config-router)# eigrp router-id 1.1.1.1
A unique ID, as in OSPF.
R1(config-router)# network 172.16.1.0 0.0.0.255
Run EIGRP on the LAN port — the same wildcard idea as OSPF, but no area.
R1(config-router)# network 10.0.0.0 0.0.0.3
R1(config-router)# network 10.0.0.8 0.0.0.3
Run EIGRP on both links.
R1(config-router)# passive-interface g0/0/0
No EIGRP hellos to the LAN.
R1(config-router)# no auto-summary
Advertise the real subnets, not a classful summary.
Check it: show ip eigrp neighbors lists R2 and R3; the routes appear as D … [90/3072].
Watch out: A different AS number (100 vs 10) means no neighbours at all. EIGRP routes show as D, not E.
Notes: Fill in the comparison table from the original Lab 3 part E: code, AD, metric to 172.16.2.0, failover time, lines of configuration per router. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 59: How to troubleshoot routing
07 • ROUTING • LAB 3
Goal: Work bottom-up: interfaces first, then neighbours, then routes — in both directions.
Symptom | Check with | Likely fix
Interface down | show ip interface brief | no shutdown, the right cable, the same subnet at both ends
No OSPF or EIGRP neighbours | show ip protocols, show ip ospf neighbor | Same area / same AS; correct network statements; router links not passive
A network is missing from the table | show ip route on each router | Add the missing network statement on the router that owns it
Ping works one way only | show ip route on the far router | Add the return route — both directions are needed
Traffic takes an odd path | show ip route (look at the codes) | Lowest distance wins: remove the old method (no router rip)
Ping fails part-way | tracert from a PC | The fault is just after the last router that answered
Tip: Ping each neighbour first: if two directly connected routers can’t ping, no routing protocol will work.
Notes: This table is the basis of the Lab 8 troubleshooting challenge. Ask trainees to log each fault as: symptom → test → finding → fix → re-test.

## Slide 60: How to secure switches and routers
08
Allow only known devices on switch ports, filter traffic with ACLs, and share one public address with NAT. (Lab 6)
In this part, learn how to:
set up the security lab
lock switch ports
understand ACL rules
write standard and extended ACLs
test and read an ACL
configure PAT and static NAT
Notes: Lab 6 implements a written policy. Read the policy with the class first and ask which tool enforces each line: port security, a standard ACL on the VTY lines, an extended ACL, PAT, static NAT.

## Slide 61: How to set up the security lab (Lab 6 topology)
08 • SECURITY & NAT • LAB 6
Goal: One router joins the STAFF LAN, the STUDENT LAN and the ISP. A written policy says who may reach what.
ISP
203.0.113.1
Internet server
198.51.100.10
R1
S1
S2
ADMIN-PC
.10.10
STAFF-PC
.10.11
WEB-INT
.10.100
STU-PC1
.20.15
G0/0/2 203.0.113.2 /29
G0/0/0 192.168.10.1
G0/0/1 192.168.20.1
STAFF 192.168.10.0/24
STUDENTS 192.168.20.0/24
The policy
Only ADMIN-PC may SSH to R1.
Students may browse the internal web server — nothing else in STAFF.
Everyone reaches the Internet through one public address (PAT).
WEB-INT is published to the Internet as 203.0.113.5 (static NAT).
Only registered devices may use the staff switch ports.
R1 also needs a default route: ip route 0.0.0.0 0.0.0.0 203.0.113.1.
Notes: The ISP link is a /29 so that the static NAT address 203.0.113.5 sits in the same subnet as R1’s outside interface — the ISP router then reaches it without extra routes. G0/0/2 on a 4331 needs a GLC-T module.

## Slide 62: How to lock switch ports with port security
08 • SECURITY & NAT • LAB 6
Goal: Only the registered PC may use each staff port. Any other device shuts the port down.
● ● ● S1 — type the white text, then press Enter
What it does
S1(config)# interface range fa0/1 - 3
The three staff ports.
S1(config-if-range)# switchport mode access
Port security only works on a port fixed as access (or trunk), not left dynamic.
S1(config-if-range)# switchport port-security
Turn the feature on (default: 1 MAC address, violation shutdown).
S1(config-if-range)# switchport port-security maximum 1
One device per port. (Use 2 for an IP phone with a PC behind it.)
S1(config-if-range)# switchport port-security mac-address sticky
Learn the first device’s MAC and write it into the running-config automatically.
S1(config-if-range)# switchport port-security violation shutdown
An unknown device shuts the port (err-disabled). Other modes: restrict (drop + log), protect (drop quietly).
Check it: Ping from each PC first, then show port-security interface fa0/2 → Secure-up, 1 sticky MAC.
Watch out: Recover an err-disabled port: remove the rogue device, then shutdown and no shutdown on the port.
Notes: Violation test: swap STAFF-PC for a “ROGUE” laptop, ping, and Fa0/2 goes err-disabled (red). Save the config after the sticky MACs are learned, or they are lost at reload. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 63: How to understand ACL rules before you write one
08 • SECURITY & NAT
Goal: An access control list (ACL) is a list of permit/deny rules that a router checks for every packet.
Rules are checked top-down; the first match wins and the rest are skipped.
Every ACL ends with a hidden deny any — include at least one permit.
Standard (1–99): checks the source only → place it near the destination.
Extended (100–199 or a name): source, destination, protocol and port → place it near the source.
Wildcards: 0 = must match, 1 = ignore. 0.0.0.255 = a /24, host 10.1.1.5 = one address, any = all.
One ACL per interface, per direction (in or out).
Packet arrives
Line 10 matches?
yes
PERMIT
no
Line 20 matches?
yes
DENY
no
Line 30 matches?
yes
PERMIT
no
No match at all → hidden deny any
Once a line matches, the packet is permitted or dropped — later lines are never read.
Notes: Walk a few packets through the flow chart. The order trap: a broad deny above a specific permit blocks everything the permit was meant to allow.

## Slide 64: How to let only the admin PC manage the router
08 • SECURITY & NAT • LAB 6
Goal: A standard ACL on the VTY lines: only ADMIN-PC (192.168.10.10) may open an SSH session to R1.
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# access-list 10 remark ONLY ADMIN-PC MAY MANAGE R1
A note stored with the ACL, for the next administrator.
R1(config)# access-list 10 permit host 192.168.10.10
Permit only the admin PC’s address. The hidden deny any blocks everyone else.
R1(config)# line vty 0 4
The remote-access lines.
R1(config-line)# access-class 10 in
Check each incoming SSH session against ACL 10. On lines it is access-class; on interfaces it is ip access-group.
Check it: ADMIN-PC: ssh -l netadmin 192.168.10.1 works. STAFF-PC: the connection is refused.
Watch out: Test from ADMIN-PC before you log out — a wrong address locks everyone out (the console still works).
Notes: SSH must already be configured on R1 (part 03). This is the “standard ACL near the destination” rule in action: the destination is R1 itself. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 65: How to filter traffic with an extended named ACL
08 • SECURITY & NAT • LAB 6
Goal: Students may open the intranet web server, but nothing else in the STAFF LAN. Everything else is allowed.
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# ip access-list extended STUDENT-POLICY
Create a named extended ACL. The prompt becomes (config-ext-nacl)#.
R1(config-ext-nacl)# remark Students may browse the intranet only
A note stored with the ACL.
R1(config-ext-nacl)# permit tcp 192.168.20.0 0.0.0.255 host 192.168.10.100 eq 80
Students (192.168.20.x) may open web pages (TCP port 80) on the web server.
R1(config-ext-nacl)# deny ip 192.168.20.0 0.0.0.255 192.168.10.0 0.0.0.255
Anything else from students to the staff LAN is blocked.
R1(config-ext-nacl)# permit ip any any
Everything else (e.g. the Internet) is allowed — this beats the hidden deny any.
R1(config-ext-nacl)# exit
R1(config)# interface g0/0/1
R1(config-if)# ip access-group STUDENT-POLICY in
Check packets as they enter R1 from the student LAN — close to the source.
Check it: Run the tests on the next slide; show access-lists counts the matches of each line.
Watch out: Order matters: if the deny line came first, even the web page would be blocked.
Notes: Read each line aloud as a sentence: “permit TCP from any student to host .100, port 80”. Long lines wrap in the slide, but in the CLI each permit/deny is typed on one line. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 66: How to test and read an ACL
08 • SECURITY & NAT • LAB 6
Goal: Prove the policy with planned tests, then read the match counters to see which line caught each packet.
R1 › CLI
R1# show access-lists
Standard IP access list 10
10 permit host 192.168.10.10 (2 match(es))
Extended IP access list STUDENT-POLICY
10 permit tcp 192.168.20.0 0.0.0.255 host 192.168.10.100 eq www (4 match(es))
20 deny ip 192.168.20.0 0.0.0.255 192.168.10.0 0.0.0.255 (8 match(es))
30 permit ip any any (12 match(es))
Test from STU-PC1 | Expected | Because of
Browser: http://192.168.10.100 | Page loads | line 10 (TCP 80)
ping 192.168.10.100 | Fails | line 20
ping 192.168.10.11 | Fails | line 20
Browser: http://198.51.100.10 | Page loads | line 30 (after NAT)
Reading the output
eq www = port 80. 10, 20, 30 are sequence numbers: insert a line with 15 permit …, remove one with no 20.
Think
STAFF-PC → STU-PC1 ping fails too. Why? The reply hits line 20.
Notes: ACLs are stateless: the reply from STU-PC1 enters G0/0/1 and is checked like any other packet, so line 20 drops it. Ask the class how they would allow staff to ping students (permit icmp echo-reply before line 20).

## Slide 67: How to share one public address with PAT
08 • SECURITY & NAT • LAB 6
Goal: All inside PCs reach the Internet through R1’s single public address, told apart by port numbers (NAT overload).
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# interface g0/0/0
R1(config-if)# ip nat inside
The STAFF LAN port is on the inside (private addresses).
R1(config-if)# interface g0/0/1
R1(config-if)# ip nat inside
The STUDENT LAN port is inside too.
R1(config-if)# interface g0/0/2
R1(config-if)# ip nat outside
R1(config-if)# exit
The ISP link is the outside (public address 203.0.113.2).
R1(config)# access-list 1 permit 192.168.10.0 0.0.0.255
R1(config)# access-list 1 permit 192.168.20.0 0.0.0.255
Choose which inside addresses may be translated. Here the ACL selects — it does not filter.
R1(config)# ip nat inside source list 1 interface g0/0/2 overload
Translate those sources to G0/0/2’s public address and share it by port number: PAT.
Check it: Browse http://198.51.100.10 from a PC, then run show ip nat translations on R1.
Watch out: NAT “does nothing”? Usually inside and outside are swapped, or the default route to the ISP is missing.
Notes: Follow one packet: 192.168.20.15:1025 becomes 203.0.113.2:1025 on the way out; the reply to 203.0.113.2:1025 is translated back. A second PC using port 1025 gets another public port — that is how thousands of users share one address. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 68: How to publish an internal server with static NAT
08 • SECURITY & NAT • LAB 6
Goal: A permanent one-to-one mapping lets Internet users reach the internal web server at a public address.
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# ip nat inside source static 192.168.10.100 203.0.113.5
Internet users who browse to 203.0.113.5 reach WEB-INT (192.168.10.100), and its replies leave as 203.0.113.5.
R1# show ip nat translations
Show the NAT table (below).
R1 › CLI
Pro Inside global Inside local Outside local Outside global
--- 203.0.113.5 192.168.10.100 --- ---
tcp 203.0.113.2:1025 192.168.20.15:1025 198.51.100.10:80 198.51.100.10:80
Inside local
The private address of the inside host, e.g. 192.168.10.100.
Inside global
The public address it becomes on the Internet, e.g. 203.0.113.5.
Outside local / global
The Internet host — the same in this lab: 198.51.100.10.
Check it: From the Internet server’s side, browse http://203.0.113.5: the WEB-INT page appears.
Watch out: Use a public address no other device uses — here one from R1’s ISP subnet (203.0.113.0/29).
Notes: Static NAT is two-way and permanent; PAT entries appear only while a conversation is active. Clear dynamic entries with clear ip nat translation * if trainees want to watch them appear again. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 69: How to add redundancy without loops
09
Extra links between switches keep users online when a cable fails — if Spanning Tree controls them. EtherChannel turns parallel links into one. (Lab 7)
In this part, learn how to:
understand Spanning Tree and the lab
choose the root bridge, PortFast and BPDU Guard
read show spanning-tree
bundle links with LACP EtherChannel
Notes: Lab 7: three 2960 switches in a triangle (cross-over cables), S1–S2 joined by two links that become an EtherChannel. PC1 on S3 Fa0/10 and PC2 on S1 Fa0/10, both in VLAN 10. All inter-switch links are trunks.

## Slide 70: How to understand Spanning Tree before you configure it
09 • STP & ETHERCHANNEL • LAB 7
Goal: Redundant links are good for uptime but create loops. Spanning Tree keeps one path active and the others on standby.
Extra links = backup paths — but they also create loops.
A loop is deadly at Layer 2: frames have no TTL, so broadcasts circle for ever (a broadcast storm) and the network freezes.
STP elects a root bridge (the lowest bridge ID) and keeps the best path from every switch to it.
Every other path is blocked — but kept ready.
If the active path fails, the blocked port starts forwarding: in 1–2 seconds with Rapid PVST+.
Think of it like this
A ring road with one barrier: traffic never circles, and if the main road closes the barrier lifts.
S1
S2
S3
PC2
VLAN 10
PC1
VLAN 10
ROOT
Po1 = Fa0/1 + Fa0/2
Fa0/3
Fa0/4
S3 Fa0/4 BLOCKED (backup)
Cross-over cables between switches; all switch–switch links are trunks.
Notes: Demonstrate a broadcast storm only in theory — in Packet Tracer STP is on by default, which is why some ports show amber for about 30 seconds when you connect them. Ask: which port would you block to break the triangle? STP decides it for you.

## Slide 71: How to set the root bridge, PortFast and BPDU Guard
09 • STP & ETHERCHANNEL • LAB 7
Goal: Choose the centre of the network yourself, start PC ports instantly, and protect them from rogue switches.
● ● ● S1 / S2 / S3 — type the white text, then press Enter
What it does
S1(config)# spanning-tree mode rapid-pvst
Use Rapid PVST+: it recovers in about 1–2 s instead of 30–50 s. Type it on every switch.
S1(config)# spanning-tree vlan 1,10,20 root primary
Make S1 the root bridge for these VLANs (priority 24576) — your choice, not luck.
S2(config)# spanning-tree vlan 1,10,20 root secondary
S2 takes over as root if S1 fails (priority 28672).
S3(config)# interface fa0/10
S3(config-if)# spanning-tree portfast
The PC port starts forwarding at once — no 30-second wait. Only on ports to end devices!
S3(config-if)# spanning-tree bpduguard enable
If someone plugs a switch into this PC port, the port shuts down (err-disabled) before a loop forms.
Check it: show spanning-tree vlan 10 on S1 says “This bridge is the root”.
Watch out: Never use PortFast on a port that connects to another switch — it can create a temporary loop.
Notes: Without root primary, the switch with the lowest MAC address wins by accident — often the oldest, slowest switch. Do the same PortFast and BPDU Guard on S1 Fa0/10 for PC2. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 72: How to read show spanning-tree
09 • STP & ETHERCHANNEL • LAB 7
Goal: Find the root, the blocked port and the edge port from one output — then prove that failover works.
S3 › CLI
S3# show spanning-tree vlan 10
VLAN0010
Spanning tree enabled protocol rstp
Root ID Priority 24586
Address 0001.4295.A7C1
Cost 19
Port 3(FastEthernet0/3)
Bridge ID Priority 32778
Interface Role Sts Cost Prio.Nbr Type
----------- ---- --- ----- -------- --------
Fa0/3 Root FWD 19 128.3 P2p
Fa0/4 Altn BLK 19 128.4 P2p
Fa0/10 Desg FWD 19 128.10 P2p Edge
Root ID priority 24586
24576 (root primary) + 10 (the VLAN number): the root is S1.
Root FWD
This switch’s best path to the root, forwarding. Cost 19 = one 100 Mbps link.
Altn BLK
The blocked backup port. It breaks the loop and waits to take over.
Desg FWD … Edge
The PC port, forwarding at once thanks to PortFast.
Test: ping -t PC1 → PC2, then shut S3 Fa0/3.
Notes: During the failover test, Fa0/4 changes from Altn BLK to Root FWD and only 1–3 replies are lost. Stop ping -t with Ctrl+C. Repeat the test with classic STP (spanning-tree mode pvst) to compare recovery time.

## Slide 73: How to bundle links with an LACP EtherChannel
09 • STP & ETHERCHANNEL • LAB 7
Goal: Join the two S1–S2 links into one logical link: double the bandwidth, and STP blocks neither of them.
● ● ● S1 — type the white text, then press Enter
What it does
S1(config)# interface range fa0/1 - 2
The two parallel links between S1 and S2.
S1(config-if-range)# channel-group 1 mode active
Bundle them as Port-channel 1 using LACP. active proposes the bundle; the other end must be active or passive.
S1(config-if-range)# exit
Back to global mode. Interface Port-channel1 now exists.
S1(config)# interface port-channel 1
S1(config-if)# switchport mode trunk
From now on configure the bundle, not its member ports. Here it becomes one logical trunk.
! Repeat the same commands on S2
A bundle needs both ends configured.
S1# show etherchannel summary
Look for Po1(SU) (S = Layer 2, U = in use) with both members marked (P) = bundled.
Check it: Both switches show Po1(SU) with Fa0/1(P) Fa0/2(P); STP now treats Po1 as one link.
Watch out: Members must match: speed, duplex, access/trunk mode and allowed VLANs. (I) or (s) = a mismatch.
Notes: LACP modes: active + active or active + passive form a bundle; passive + passive never does. Mode on forces a bundle without negotiation and must be on at both ends. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 74: How to manage devices and add IPv6
10
Keep every device on the same clock, send logs to a server, discover neighbours, back up configurations — and switch on IPv6. (Labs 9 and 10)
In this part, learn how to:
set the time and send logs (NTP, Syslog)
discover neighbours and allow monitoring (CDP, LLDP, SNMP)
back up and restore with TFTP
configure basic IPv6 addressing and routing
Notes: Lab 9 uses the Lab 4 (DHCP) file with SRV1 (192.168.50.10) on the server LAN: switch on its NTP, SYSLOG and TFTP services first. Lab 10 (IPv6) uses a separate two-router file (R1–R2 with one LAN each).

## Slide 75: How to set the time and send logs to a server
10 • MANAGEMENT & IPV6 • LAB 9
Goal: Logs are only useful if every device has the right time and sends its messages to one place.
● ● ● R1 — type the white text, then press Enter
What it does
R1# clock set 09:00:00 6 October 2026
Set the clock by hand (privileged mode). Fine for one device; NTP keeps every device in step.
R1(config)# ntp server 192.168.50.10
Take the time from the NTP server (SRV1), so the logs of all devices line up.
R1(config)# service timestamps log datetime msec
Stamp every log message with the date and time.
R1(config)# logging host 192.168.50.10
Copy every log message to the Syslog service on SRV1.
R1(config)# logging trap debugging
Send all severity levels (0–7) — fine in a lab. Real networks usually send informational (6).
Check it: show ntp status → “Clock is synchronized”. SRV1 › Services › SYSLOG lists R1’s messages.
Watch out: Switch the services on first: SRV1 › Services › NTP and SYSLOG must both be On.
Notes: NTP can take a minute to synchronise — use Fast Forward Time. Generate a log message on purpose (shut and no shut an interface) and find it on SRV1 with the correct timestamp. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 76: How to discover neighbours and allow monitoring
10 • MANAGEMENT & IPV6 • LAB 9
Goal: CDP and LLDP show who is connected where; SNMP lets a monitoring tool read each device’s status.
● ● ● R1 — type the white text, then press Enter
What it does
R1# show cdp neighbors
Lists the Cisco devices plugged into R1: name, model, and the local and remote ports that join them.
R1# show cdp neighbors detail
Adds each neighbour’s IP address and IOS version — ideal for mapping a network you don’t know.
R1(config)# lldp run
R1# show lldp neighbors
LLDP is the open-standard version of CDP (works with other vendors). It is off by default.
R1(config)# snmp-server community KNP-RO ro
Monitoring tools that know the community “KNP-RO” may read R1’s information. ro = read-only.
R1(config)# snmp-server location KNP-ICT-MDF-Rack1
R1(config)# snmp-server contact ict@knp.ac.ke
Where the device is and who looks after it — shown on monitoring dashboards.
Check it: PC › Desktop › MIB Browser: Advanced… (R1’s address, read community KNP-RO), then Get a value.
Watch out: CDP and LLDP reveal device details: switch them off on ports facing the Internet (no cdp enable).
Notes: Mapping exercise: give trainees an unlabelled topology and let them draw it using only show cdp neighbors on each device. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 77: How to back up and restore a configuration with TFTP
10 • MANAGEMENT & IPV6 • LAB 9
Goal: Keep a copy of every configuration on a server, so a replaced or broken router is restored in minutes.
R1 › CLI (sample)
R1# copy running-config tftp:
Address or name of remote host []? 192.168.50.10
Destination filename [R1-confg]? R1-2026-10-06.cfg
Writing running-config...!!
[OK - 1052 bytes]
R1# copy tftp: running-config
Address or name of remote host []? 192.168.50.10
Source filename []? R1-2026-10-06.cfg
Destination filename [running-config]?
! press Enter to accept
1
Prepare the server
SRV1 › Services › TFTP → On.
2
Back up
copy running-config tftp: → server address → a file name with device and date.
3
Check
The file appears in SRV1’s TFTP file list.
4
Restore
copy tftp: running-config when a router is replaced or a change goes wrong.
Watch out: TFTP has no password and no encryption — real networks use SCP or SFTP. Back up after every change.
Notes: A restore merges the file into the running-config; then save it with copy running-config startup-config. Good file names (device + date) make it easy to roll back to a known good version.

## Slide 78: How to configure basic IPv6 on a router (1 of 2)
10 • MANAGEMENT & IPV6 • LAB 10
Goal: Give R1’s ports IPv6 addresses and turn on IPv6 routing, so PCs can configure themselves (SLAAC).
● ● ● R1 — type the white text, then press Enter
What it does
R1(config)# ipv6 unicast-routing
Turn on IPv6 routing (off by default). Without it R1 won’t forward IPv6 or advertise its prefixes, so SLAAC fails.
R1(config)# interface g0/0/0
The LAN port.
R1(config-if)# ipv6 address 2001:db8:acad:1::1/64
A global unicast address. /64 is the standard prefix for every LAN — SLAAC needs 64 host bits.
R1(config-if)# ipv6 address fe80::1 link-local
A short, easy link-local address. PCs use it as their default gateway.
R1(config-if)# no shutdown
Switch the port on (if it is not on already).
R1(config-if)# interface g0/0/1
R1(config-if)# ipv6 address 2001:db8:acad:12::1/64
R1(config-if)# ipv6 address fe80::1 link-local
R1(config-if)# no shutdown
The same on the link to R2. (R2 uses ::2 and fe80::2; its LAN is 2001:db8:acad:2::/64.)
Check it: show ipv6 interface brief → each port up/up with its FE80::1 and 2001:DB8:… addresses.
Watch out: Type the colons carefully: :: may appear only once in an address.
Notes: IPv4 and IPv6 can run on the same ports at the same time (dual stack). Remind trainees that IPv6 never uses broadcasts — Router Advertisements are multicasts. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 79: How to configure basic IPv6 on a router (2 of 2)
10 • MANAGEMENT & IPV6 • LAB 10
Goal: Add routes between the IPv6 LANs, let the PCs configure themselves, and test end to end.
● ● ● R1 / R2 / PC1 — type the white text, then press Enter
What it does
R1(config)# ipv6 route 2001:db8:acad:2::/64 2001:db8:acad:12::2
A static IPv6 route to R2’s LAN via R2’s address on the shared link — like IPv4, with a prefix length.
R2(config)# ipv6 route ::/0 2001:db8:acad:12::1
An IPv6 default route on R2 (::/0 = every address), back to R1.
! PC1: IP Configuration › IPv6 › Automatic
The PC builds its own address from R1’s /64 prefix (SLAAC) and uses fe80::1 as its gateway.
R1# show ipv6 route
C, L and S routes for IPv6 — read it just like the IPv4 table.
C:\> ping 2001:db8:acad:2::10
From PC1, ping PC2 (static 2001:db8:acad:2::10/64, gateway fe80::2).
Check it: tracert 2001:db8:acad:2::10 from PC1 passes R1 and then R2.
Watch out: SLAAC fails without ipv6 unicast-routing — R1 never sends the Router Advertisements PCs need.
Notes: Extension for fast trainees: replace the static routes with OSPFv3, or add IPv4 to the same ports for a dual-stack network. Click-to-reveal: each click shows the next explanation; the last click shows Check it and Watch out. Before each click, ask a trainee to predict what the command does.

## Slide 80: How to test and troubleshoot your network
11
A calm, systematic method finds any fault: climb the ping ladder, ask the right show command, fix one thing, re-test, and log it.
In this part, learn how to:
climb the ping ladder
choose the right show command
fix the most common Packet Tracer mistakes
keep a troubleshooting log
Notes: This part supports the Lab 8 troubleshooting challenge: the trainer injects 6–8 faults into a working Lab 2 + Lab 3 network; pairs find, fix and log them.

## Slide 81: How to troubleshoot step by step: the ping ladder
11 • TROUBLESHOOTING
Goal: Climb from the PC itself to the far network. The first step that fails tells you where the fault is.
1
ping 127.0.0.1
the PC’s own network software works
2
ping 192.168.10.21
its own address: the network card is set up
3
ping 192.168.10.1
the gateway: cable, switch port, VLAN and router port work
4
ping 172.16.2.10
a remote PC: routing works there and back
5
ping www.knp.local
by name: DNS works
climb
Stop at the first step that fails
The fault is between that step and the one below it.
Then follow the method
Symptom: what exactly fails?
Theory: what could cause it?
Test it with a show command
Fix one thing only
Re-test, then log it
tracert shows the last router that answered — the fault is just after it.
Notes: Example: steps 1–3 work but 4 fails → the LAN is fine; look at routing (show ip route on each router, both directions). Steps 1–4 work but 5 fails → DNS (server address in the PC or the DHCP pool).

## Slide 82: How to choose the right show command
11 • TROUBLESHOOTING
Goal: Each question has one command that answers it. Learn this table and you can diagnose almost anything.
Question | Command | Look for
Are my ports up and addressed? | show ip interface brief | up / up and the right IP
What is configured? | show running-config | typos, a missing no shutdown
Which port is in which VLAN? | show vlan brief | ports beside the right VLAN
Are the trunks working? | show interfaces trunk | trunking, native VLAN, allowed VLANs
Which device is plugged in where? | show cdp neighbors | device, local port, remote port
Where did the switch learn a MAC? | show mac address-table | the MAC on the expected port
Does the router know the way? | show ip route | a C, S, O, R or D route
Did DHCP lease addresses? | show ip dhcp binding | one line per PC
Are OSPF neighbours up? | show ip ospf neighbor | FULL state
Is the ACL matching? | show access-lists | match counts going up
Is NAT translating? | show ip nat translations | inside local ↔ inside global
Is port security blocking? | show port-security interface fa0/1 | Secure-up or Secure-shutdown
Notes: Turn this into a quiz: read a question, trainees shout the command. Remember the do prefix: from config mode type do show ip interface brief.

## Slide 83: How to fix the most common Packet Tracer mistakes (1 of 2)
11 • TROUBLESHOOTING
Goal: These faults cause most “it doesn’t work” moments in class. Check them first.
Symptom | Likely cause | Fix
Red link light on a router port | The port was never switched on | no shutdown on that interface
Red link light, port is on | Wrong cable type | Straight-through between different devices; cross-over between the same kind
Amber light on a switch port | Spanning Tree is still starting the port | Wait about 30 s, or click Fast Forward Time
% Invalid input detected | A typo, or the wrong mode | Read the prompt; use ? to see what is allowed
PC cannot ping its own gateway | Wrong IP/mask/gateway, or port in the wrong VLAN | ipconfig on the PC; show vlan brief on the switch
PCs in different VLANs cannot ping | Trunk, sub-interface or gateway problem | show interfaces trunk; check encapsulation dot1Q and each PC’s gateway
Tip: Fix one thing at a time and re-test — otherwise you won’t know which change fixed it.
Notes: Ask trainees which of these they have already met. Most have met the first three in Lab 1.

## Slide 84: How to fix the most common Packet Tracer mistakes (2 of 2)
11 • TROUBLESHOOTING
Goal: More faults to rule out — from DHCP and routing to saving and hardware.
Symptom | Likely cause | Fix
PC address is 169.254.x.x | No DHCP reply | See “How to fix common DHCP problems” (part 06)
Remote network unreachable | A route is missing — often the return route | show ip route on every router along the path
Configuration gone after a reload | It was never saved | copy running-config startup-config after every working step
SSH connection refused | No RSA keys or domain name, or login instead of login local | show ip ssh; check the VTY lines
G0/0/2 missing on a 4331 | The SFP slot is empty | Power off, insert a GLC-T module, power on
The first ping loses one reply | ARP is finding the MAC address | Normal — ping again
Tip: Still stuck? Compare show running-config line by line with the slide for that skill.
Notes: The last row matters: trainees often “fix” a working network because the first ping lost one reply. Teach them to ping twice before deciding.

## Slide 85: How to keep a troubleshooting log
11 • TROUBLESHOOTING
Goal: Write down every fault as you go. The log is assessment evidence and stops you fixing the same thing twice.
# | Test / symptom | Command used | Root cause | Fix applied | Re-test
1 | PC3 cannot ping PC6 | show interfaces trunk | VLAN 30 not allowed on the trunk | switchport trunk allowed vlan add 30 | PASS
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
Watch out: Change one thing at a time, and re-test after each change.
Tip: Lab 8 scoring: 2 points for each fault fixed and logged; minus 1 for any new fault you create.
Notes: Lab 8: write a test plan (10+ tests) before touching anything, test bottom-up with the ping ladder, then log each fault in this format and write a one-page test report.

## Slide 86: How to practise and revise on your own
12
Two challenge labs that combine everything, a checklist to judge your own competence, and one-page command cards for revision.
In this part, learn how to:
build challenge lab A: VLANs, routing between them and DHCP
build challenge lab B: routing, NAT and security
check yourself against the competence list
revise with the switch and router cards
Notes: Use the challenge labs for revision before the practical CAT. Trainees should build them from a blank workspace, without the slides, then use the slides only to check.

## Slide 87: How to practise: challenge lab A — VLANs, routing and DHCP
12 • PRACTICE & QUICK REFERENCE • CHALLENGE
Goal: Rebuild Lab 2 without the slides. Time yourself: aim for under 90 minutes.
R1
DHCP + gateways
S1
S2
VLAN 10 / 20 / 30 PCs on both switches; VLAN 99 = management
Tasks — from a blank workspace
Basic set-up and SSH on R1, S1 and S2; shut unused ports.
VLANs 10 STAFF, 20 STUDENTS, 30 FINANCE, 99 MGMT on both switches.
Access ports as in the plan; trunks with native VLAN 99.
Router-on-a-stick on R1 G0/0/1 (.10, .20, .30, .99 native).
DHCP pools for VLANs 10, 20, 30 (exclude .1–.20); PCs on DHCP.
Switch management in VLAN 99; save every device.
You are competent when…
every PC leases an address from its own VLAN, PCs in different VLANs ping each other, show interfaces trunk shows native VLAN 99, SSH works and Telnet fails.
Notes: Assessment tip: watch trainees type rather than only checking the result, and ask them to explain three commands of your choice.

## Slide 88: How to practise: challenge lab B — routing, NAT and security
12 • PRACTICE & QUICK REFERENCE • CHALLENGE
Goal: Combine Lab 3 and Lab 6: OSPF inside, PAT to the ISP, and a security policy.
ISP
R1
R2
R3
Lab 3 triangle + an ISP router on R1 (203.0.113.0/29)
Tasks — from a blank workspace
Address all links (/30) and LANs; OSPF area 0 on R1, R2, R3.
R1: default route to the ISP + default-information originate.
PAT on R1 for all three LANs (inside: LAN and links; outside: ISP).
ACL: LAN 3 may reach LAN 1 only by web (TCP 80).
SSH on every router; VTY access only from one admin PC.
Port security on the LAN 1 switch; NTP and Syslog to a server.
You are competent when…
every PC reaches the ISP side, show ip nat translations shows the PCs, the ACL tests pass, OSPF neighbours are FULL, and the failover of one link is survived.
Notes: For PAT across OSPF: R1’s links to R2 and R3 are also ip nat inside, and access-list 1 must include all three LAN subnets.

## Slide 89: How to check you are competent: a self-assessment list
12 • PRACTICE & QUICK REFERENCE
Goal: Tick each line only when you can do it without the slides — this is what the practical assessment looks for.
Choose and connect the right cables
Move between IOS modes and use ?
Do the basic set-up and save it
Address router ports and a switch SVI
Set up SSH with local users
Create VLANs and access ports
Configure trunks with a native VLAN
Configure router-on-a-stick
Route between VLANs on a Layer 3 switch
Configure DHCP pools, exclusions and relay
Configure static, default and OSPF routes
Lock ports with port security
Write and apply standard and extended ACLs
Configure PAT and static NAT
Set the root bridge, PortFast, EtherChannel
Find faults with the ping ladder and show commands
Notes: Print this slide for each trainee. They tick a line only after doing the task from a blank workspace without help; anything unticked becomes their practice plan for the week.

## Slide 90: How to remember the commands: switch quick reference
12 • PRACTICE & QUICK REFERENCE
Goal: One page of the switch commands used in this workbook. The prompt shows the mode; replace the example values.
Basic set-up
hostname S1
enable secret <password>
line console 0
password <password>
login
interface vlan 99
ip address <ip> <mask>
ip default-gateway <router-ip>
copy running-config startup-config
VLANs and trunks
vlan 10
name STAFF
interface range fa0/1 - 10
switchport mode access
switchport access vlan 10
interface g0/1
switchport mode trunk
switchport trunk native vlan 99
switchport trunk allowed vlan add 40
Security, STP, EtherChannel
switchport port-security
switchport port-security maximum 1
switchport port-security mac-address sticky
switchport port-security violation shutdown
spanning-tree mode rapid-pvst
spanning-tree vlan 10 root primary
spanning-tree portfast
spanning-tree bpduguard enable
channel-group 1 mode active
Check it
show vlan brief
show interfaces trunk
show ip interface brief
show mac address-table
show port-security interface fa0/1
show spanning-tree vlan 10
show etherchannel summary
show cdp neighbors
Notes: Lines that start with a space are typed inside the interface (or line) above them. “...” means “switchport port-security” or “switchport trunk” as in the line above.

## Slide 91: How to remember the commands: router quick reference
12 • PRACTICE & QUICK REFERENCE
Goal: One page of the router commands used in this workbook. Practise until you no longer need it.
Interfaces and SSH
interface g0/0/0
ip address <ip> <mask>
no shutdown
interface g0/0/1.10
encapsulation dot1Q 10
ip domain-name <domain>
crypto key generate rsa general-keys modulus 1024
line vty 0 4
transport input ssh
login local
Routing
ip route <network> <mask> <next-hop>
ip route 0.0.0.0 0.0.0.0 <isp-address>
router ospf 10
router-id 1.1.1.1
network <network> <wildcard> area 0
passive-interface g0/0/0
router eigrp 100
router rip
ipv6 unicast-routing
DHCP, NAT, ACL
ip dhcp excluded-address <first> <last>
ip dhcp pool <NAME>
network <network> <mask>
default-router <gateway>
ip helper-address <server>
ip nat inside | ip nat outside
ip nat inside source list 1 interface g0/0/2 overload
ip access-group <ACL> in
Check it
show ip interface brief
show ip route
show ip protocols
show ip ospf neighbor
show ip dhcp binding
show ip nat translations
show access-lists
show running-config
Notes: Use these cards for timed drills: call out a task (“default route to the ISP”) and trainees write the command in 10 seconds.

## Slide 92: How to keep improving after this workbook
★
Competence comes from repetition: rebuild each lab from a blank workspace until you can do it without the slides.
Repeat
Rebuild every lab from scratch; time yourself.
Save evidence
Keep each .pkt file and config backup in your portfolio.
Read further
Cisco Networking Academy: Packet Tracer and CCNA courses; Jeremy’s IT Lab (free CCNA videos).
Ask
Bring every error message to class — they are the best lessons.
Questions?
Notes: Close by asking each trainee to name one command they will practise tonight. Remind them that the assessment is practical: they must type the configuration themselves and explain what each command does.